## Slide 1: Network Essentials
Topic 8
Notes: NOTE:
To change the image on this slide, select the picture and delete it. Then click the Pictures icon in the placeholder to insert your own image.

## Slide 2: Introduction to Computer Networks
Definition: A computer network is a collection of interconnected devices (such as computers, servers, routers, and switches) that share resources and information.
Purpose: Facilitate communication, data sharing, and resource sharing among devices.
Benefits: Improved communication, resource sharing, centralized data management, data redundancy, and enhanced security.

## Slide 3: Introduction to LAN, MAN, WAN
Local Area Network (LAN): A network that connects computers within a limited area such as a residence, school, or office building.
Metropolitan Area Network (MAN): A network that covers a larger geographic area than a LAN, typically spanning a city or a large campus.
A network that covers a broad area (e.gWide Area Network (WAN): ., any network that links across metropolitan, regional, or national boundaries).

## Slide 4: LAN, MAN & WAN

## Slide 5: Characteristics
LAN:
High data transfer rates
Limited geographical area
Relatively low cost

## Slide 6: Characteristics Cont’d
MAN:
Medium to high data transfer rates
Covers a city or large campus
Higher cost than LAN

## Slide 7: Characteristics Cont’d
WAN:
Lower data transfer rates compared to LAN and MAN
Covers large geographical areas
High cost

## Slide 8: Essential Components of a Network

## Slide 9: Network Devices
Routers: Connect different networks and direct data packets.
Switches: Connect devices within a LAN and use MAC addresses to forward data to the correct destination.
Hubs: Basic devices that connect multiple computers in a network; however, they broadcast data to all connected devices.

## Slide 10: ROUTERS, SWITCHES & HUBS

## Slide 11: Network Media
Cables: Twisted pair, coaxial, and fiber optic cables.
Wireless Media: Radio waves, microwaves, and infrared.

## Slide 13: Network Interface Cards (NICs)
Devices that connect a computer to a network, either wired or wireless.

## Slide 15: Network Design

## Slide 16: Steps in Network Design
1. Requirements Analysis: Understanding the needs of the users and the organization.
2. Planning: Determining the layout, type of network, and hardware/software requirements.
3. Implementation: Setting up the network according to the plan.
4. Testing: Ensuring the network operates as expected.
5. Maintenance: Ongoing support and updates to the network.

## Slide 17: Considerations
Scalability: The ability to grow with increasing demand.
Reliability: Ensuring consistent and dependable performance.
Security: Protecting data and resources from unauthorized access.

## Slide 18: Topologies and Cabling

## Slide 19: Network Topology
Network topology refers to the arrangement or layout of different elements (links, nodes, devices, etc.) in a computer network. It determines how data is transmitted and received between devices and impacts network performance, reliability, and scalability.

## Slide 21: Network Topologies
Bus Topology: All devices are connected to a single central cable.
Star Topology: All devices are connected to a central hub or switch.
Ring Topology: Devices are connected in a circular fashion, with each device connected to two others.
Mesh Topology: Devices are interconnected, with multiple paths between them.

## Slide 22: Bus Topology
Description: All devices (nodes) are connected to a single central cable, known as the "bus."
Data Transmission: Data travels in both directions along the bus. Each device checks the data to see if it is intended for them.
Advantages:
  Easy to implement and extend.
  Cost-effective for small networks.
Disadvantages:
  If the central cable (bus) fails, the entire network is down.
  Limited cable length and number of nodes.
  High data traffic can lead to collisions and network degradation.
Use Cases: Small networks, temporary networks, or networks where budget constraints are significant.

## Slide 23: Star Topology
Description: All devices are connected to a central hub or switch. The hub acts as a repeater for data flow.
Data Transmission: Data is sent from a device to the central hub, which then forwards it to the destination device.
Advantages:
  Easy to manage and troubleshoot.
  Failure of one device does not affect others.
  Easy to add or remove devices.
Disadvantages:
  Failure of the central hub can disable the entire network.
  Higher cost due to the need for more cables and a central hub.
Use Cases: Office networks, home networks, and environments requiring easy troubleshooting.

## Slide 24: Ring Topology
Description: Devices are connected in a circular pattern, forming a closed loop or "ring."
Data Transmission: Data travels in one direction (unidirectional) or both directions (bidirectional) around the ring. Each device has a repeater that forwards the data.
Advantages:
  Easy to identify the location of faults.
  No collisions due to unidirectional data flow.
Disadvantages:
  A failure in any device or cable can affect the entire network.
  Adding or removing devices can disrupt the network.
Use Cases: Used in token-based networks and fiber optic networks.

## Slide 25: Mesh Topology
Description: Each device is connected to every other device in the network, providing multiple paths for data.
Data Transmission: Data can be transmitted using multiple paths, increasing redundancy and reliability.
Advantages:
  Highly reliable due to multiple redundant paths.
  Failure of one connection does not affect the network.
  Good for high-traffic environments.
Disadvantages:
  Very expensive due to the large number of cables and connections.
  Complex to set up and manage.
Use Cases: Critical networks where reliability is crucial, such as military or financial networks.

## Slide 26: Tree Topology (Hierarchical Topology)
Description: Combination of star and bus topologies. A central "root" node is connected to one or more nodes, which in turn are connected to other nodes in a hierarchical manner.
Data Transmission: Data travels from the root node through the hierarchy.
Advantages:
  Scalable and easy to manage.
  Failure of one segment does not affect the entire network.
Disadvantages:
  If the root node fails, the entire network can be affected.
  Complex cabling and setup.
Use Cases: Large organizations with hierarchical data flow.

## Slide 27: Hybrid Topology
Description: A combination of two or more different topologies (e.g., star-bus, star-ring).
Data Transmission: Depends on the combination of topologies used.
Advantages:
  Flexible and scalable.
  Can be tailored to suit specific needs.
Disadvantages:
  Complex to design, implement, and manage.
  Expensive due to multiple topologies being combined.
Use Cases: Large, complex networks like data centers, campus networks, and large enterprises.

## Slide 28: Types of Cabling
Twisted Pair: Commonly used in LANs; includes categories like Cat5, Cat5e, Cat6.
Coaxial Cable: Used for cable television and early Ethernet networks.
Fiber Optic Cable: Uses light to transmit data; provides higher speed and greater distance.

## Slide 29: Connectivity Devices
Routers: Connect different networks and route data between them.
Switches: Connect devices within a single network and manage data traffic efficiently.
Access Points: Provide wireless connectivity to a wired network.
Gateways: Connect networks using different protocols.

## Slide 30: Installation & Configuration of Network Devices

## Slide 31: Installation Steps
1. Physical Setup: Connecting devices and cabling.
2. Configuring Devices: Setting IP addresses, subnets, and other network settings.
3. Testing Connectivity: Ensuring devices can communicate.

## Slide 32: Configuration Tools
Command Line Interfaces (CLI): Used for configuring network devices.
Web Interfaces: Browser-based tools for device configuration.

## Slide 33: CLI: Configuration
IPConfig: This ipconfig command is used for finding the IP address and default gateway of your network.
NETSTAT: netstat is a command-line network utility that displays network connections for Transmission Control Protocol, routing tables, and a number of network interface and network protocol statistics.
NSLOOKUP: nslookup is a network administration command-line tool for querying the Domain Name System to obtain the mapping between domain name and IP address, or other DNS records.
traceroute and tracert: are diagnostic command-line interface commands for displaying possible routes and transit delays of packets across an Internet Protocol network. The command reports the round-trip times of the packets received from each successive host along the route to a destination.
Ping: is a computer network administration software utility used to test the reachability of a host on an Internet Protocol network.

## Slide 34: CLI: Configuration
The ARP: Address Resolution Protocol command is used to access the mapping structure of IP addresses to the MAC address. This provides us with a better understanding of the transmission of packets in the network channel.
getmac (get mac address): This command returns the MAC address from all the network cards on a system.
HOSTNAME: For Linux users, hostname is a commonly used networking command in cmd that helps set and view the hostname registered to a system. HostName. The Windows HostName network command will simply display the current name of your Windows computer.
Netsh: or network shell, is a command-line utility included in Microsoft's Windows NT line of operating systems beginning with Windows 2000. It allows local or remote configuration of network devices such as the interface.

## Slide 35: Protocols

## Slide 36: Network Protocols
A network protocol: is a set of rules outlining how connected devices communicate across a network to exchange information easily and safely.
Protocols ensure that devices on a network can communicate with each other, regardless of differences in their internal processes, hardware, or software.
They play a crucial role in enabling reliable and efficient communication between devices, such as computers, routers, switches, and servers, in local or wide-area networks (LANs or WANs) and across the internet.

## Slide 37: Network Protocols
TCP/IP (Transmission Control Protocol/Internet Protocol): Foundation of the Internet. Provides reliable, ordered, and error-checked delivery.
UDP (User Datagram Protocol): Lightweight, connectionless protocol. Faster but less reliable.
HTTP/HTTPS (Hypertext Transfer Protocol/Secure): Protocols for web communication; HTTPS includes SSL/TLS for security.
FTP (File Transfer Protocol): Used for transferring files between systems.
SMTP (Simple Mail Transfer Protocol): Protocol for sending emails.
DNS (Domain Name System): Translates domain names to IP addresses.
SNMP (Simple Network Management Protocol): Manages and monitors network devices.

## Slide 38: Addressing
Addressing in computer networks refers to the methods and schemes used to identify devices, nodes, or hosts on a network uniquely.
Addressing is crucial for ensuring that data packets are transmitted accurately from a source to a destination across a network.
It enables devices to locate and communicate with each other on both local and wide-area networks.

## Slide 39: Addressing
IP Addressing: Assigning unique addresses to devices on a network.
Subnetting: Dividing a network into smaller segments.

## Slide 46: Implementing a Peer to Peer Network
Peer to Peer (P2P) Networks: A network where each computer can act as both a client and a server.
Setup: Connecting computers directly via a switch or hub without a dedicated server.

## Slide 48: Advantages and Disadvantages
Advantages: Simple to set up and cost-effective.
Disadvantages: Less control and security compared to server-based networks.

## Slide 49: Network Maintenance and Troubleshooting

## Slide 50: Maintenance
Regular Updates: Keeping software and firmware up to date.
Monitoring: Using tools to monitor network performance and detect issues.
Backup: Regularly backing up network configurations and data.

## Slide 51: Troubleshooting Steps
Identify the Problem: Gathering information and defining the issue.
Develop a Hypothesis: Formulating possible causes.
Test the Hypothesis: Trying solutions to see if they resolve the issue.
Document: Recording the problem and solution for future reference.

## Slide 52: Making Network Cables (Crossed, Straight)

## Slide 53: Tools and Materials
Tools: Crimping tool, cable tester, wire stripper.
Materials: Twisted pair cables (Cat5e, Cat6), RJ45 connectors.

## Slide 54: Straight-Through Cables
Usage: Connecting different types of devices (e.g., computer to switch).
Wiring: Both ends use the same wiring standard (either T568A or T568B).

## Slide 55: Crossover Cables
Usage: Connecting similar devices (e.g., computer to computer).
Wiring: One end uses T568A and the other end uses T568B.

## Slide 57: VIDEO LINKS
https://youtu.be/Uw8FSXx4dnU
https://youtu.be/NWhoJp8UQpo
https://youtu.be/2OLeNqsNATQ
https://youtu.be/-bQjrDirT6g

## Slide 58: THANK you