## Slide 1: Network Essentials
Topic 8
Notes: NOTE:
To change the image on this slide, select the picture and delete it. Then click the Pictures icon in the placeholder to insert your own image.

## Slide 2: Introduction to Computer Networks
Definition: A computer network is a collection of interconnected devices (computers, servers, printers, etc.) that communicate and share resources (data, applications, hardware, internet connections) through communication channels.

## Slide 3: Purpose of Networking
Resource sharing – printers, files, and internet.
Communication – email, chat, video conferencing.
Data sharing – transfer of information between systems.
Centralized management – managing data or systems from one point
Benefits: Improved communication, resource sharing, centralized data management, data redundancy, and enhanced security.

## Slide 4: Types of Networks
1. Personal Area Network (PAN)
  Very small network for personal devices.
  Example: Bluetooth connection between phone and laptop.
2. Local Area Network (LAN)
  Covers a small geographic area (office, school).
  High speed and low cost.
  Example: Office network connecting several PCs.

## Slide 5: Types of Networks Ctnd
3. Metropolitan Area Network (MAN)
  Connects multiple LANs within a city.
  Example: Network connecting branches of a university in one city.
4. Wide Area Network (WAN)
  Covers a large geographical area.
  Uses public transmission media like telephone lines or satellites.
  Example: The Internet.

## Slide 6: LAN, MAN & WAN

## Slide 7: Characteristics
LAN:
  High data transfer rates
  Limited geographical area
  Relatively low cost

## Slide 8: Characteristics Cont’d
MAN:
  Medium to high data transfer rates
  Covers a city or large campus
  Higher cost than LAN

## Slide 9: Characteristics Cont’d
WAN:
  Lower data transfer rates compared to LAN and MAN
  Covers large geographical areas
  High cost

## Slide 10: Implementing a Peer to Peer Network
Peer to Peer (P2P) Networks: A network where each computer can act as both a client and a server.
Setup: Connecting computers directly via a switch or hub without a dedicated server.

## Slide 12: Advantages and Disadvantages
Advantages: Simple to set up and cost-effective.
Disadvantages: Less control and security compared to server-based networks.

## Slide 13: Network DEVICES

## Slide 14
Device | Function
1. Hub | Simple device that broadcasts signals/data to all ports.
2. Switch | Sends data only to the intended device; improves performance.
3. Router | Routes data between different networks.
4. Bridge | Connects and filters traffic between two LAN segments.
5. Gateway | Acts as an entry/exit point for networks using different protocols.
6. Access Point | Provides wireless connectivity (Wi-Fi).
7. Modem | Converts digital signals to analog and vice versa for internet access.

## Slide 15: ROUTERS, SWITCHES & HUBS

## Slide 16: Network Communication Media
1. Guided Media (Wired)
  Twisted Pair Cable (UTP/STP)
  Coaxial Cable
  Fiber Optic Cable
2. Unguided Media (Wireless)
  Radio waves
  Microwave
  Infrared
  Satellite communication

## Slide 17: Wired Media
Twisted Pair: Commonly used in LANs; includes categories like Cat5, Cat5e, Cat6.
Coaxial Cable: Used for cable television and early Ethernet networks.
Fiber Optic Cable: Uses light to transmit data; provides higher speed and greater distance.

## Slide 20: Network Interface Cards (NICs)
Devices that connect a computer to a network, either wired or wireless.

## Slide 22: NETWORK Topologies

## Slide 23: Network Topology
Network topology refers to the arrangement or layout of different elements (links, nodes, devices, etc.) in a computer network.
It determines how data is transmitted and received between devices and impacts network performance, reliability, and scalability.

## Slide 25: Bus Topology
Description: All devices (nodes) are connected to a single central cable, known as the "bus."
Data Transmission: Data travels in both directions along the bus. Each device checks the data to see if it is intended for them.
Advantages:
  Easy to implement and extend.
  Cost-effective for small networks.
Disadvantages:
  If the central cable (bus) fails, the entire network is down.
  Limited cable length and number of nodes.
  High data traffic can lead to collisions and network degradation.
Use Cases: Small networks, temporary networks, or networks where budget constraints are significant.

## Slide 26: Star Topology
Description: All devices are connected to a central hub or switch. The hub acts as a repeater for data flow.
Data Transmission: Data is sent from a device to the central hub, which then forwards it to the destination device.
Advantages:
  Easy to manage and troubleshoot.
  Failure of one device does not affect others.
  Easy to add or remove devices.
Disadvantages:
  Failure of the central hub can disable the entire network.
  Higher cost due to the need for more cables and a central hub.
Use Cases: Office networks, home networks, and environments requiring easy troubleshooting.

## Slide 27: Ring Topology
Description: Devices are connected in a circular pattern, forming a closed loop or "ring."
Data Transmission: Data travels in one direction (unidirectional) or both directions (bidirectional) around the ring. Each device has a repeater that forwards the data.
Advantages:
  Easy to identify the location of faults.
  No collisions due to unidirectional data flow.
Disadvantages:
  A failure in any device or cable can affect the entire network.
  Adding or removing devices can disrupt the network.
Use Cases: Used in token-based networks and fiber optic networks.

## Slide 28: Mesh Topology
Description: Each device is connected to every other device in the network, providing multiple paths for data.
Data Transmission: Data can be transmitted using multiple paths, increasing redundancy and reliability.
Advantages:
  Highly reliable due to multiple redundant paths.
  Failure of one connection does not affect the network.
  Good for high-traffic environments.
Disadvantages:
  Very expensive due to the large number of cables and connections.
  Complex to set up and manage.
Use Cases: Critical networks where reliability is crucial, such as military or financial networks.

## Slide 29: Tree Topology (Hierarchical Topology)
Description: Combination of star and bus topologies. A central "root" node is connected to one or more nodes, which in turn are connected to other nodes in a hierarchical manner.
Data Transmission: Data travels from the root node through the hierarchy.
Advantages:
  Scalable and easy to manage.
  Failure of one segment does not affect the entire network.
Disadvantages:
  If the root node fails, the entire network can be affected.
  Complex cabling and setup.
Use Cases: Large organizations with hierarchical data flow.

## Slide 30: Hybrid Topology
Description: A combination of two or more different topologies (e.g., star-bus, star-ring).
Data Transmission: Depends on the combination of topologies used.
Advantages:
  Flexible and scalable.
  Can be tailored to suit specific needs.
Disadvantages:
  Complex to design, implement, and manage.
  Expensive due to multiple topologies being combined.
Use Cases: Large, complex networks like data centers, campus networks, and large enterprises.

## Slide 31: Network Design

## Slide 32: Steps in Network Design
1. Requirements Analysis: Understanding the needs of the users and the organization.
2. Planning: Determining the layout, type of network, and hardware/software requirements.
3. Implementation: Setting up the network according to the plan.
4. Testing: Ensuring the network operates as expected.
5. Maintenance: Ongoing support and updates to the network.

## Slide 33: Considerations
Scalability: The ability to grow with increasing demand.
Reliability: Ensuring consistent and dependable performance.
Security: Protecting data and resources from unauthorized access.

## Slide 34: Installation & Configuration of Network Devices

## Slide 35: Installation Steps
1. Physical Setup: Connecting devices and cabling.
2. Configuring Devices: Setting IP addresses, subnets, and other network settings.
3. Testing Connectivity: Ensuring devices can communicate.

## Slide 36: Configuration Tools
Command Line Interfaces (CLI): Used for configuring network devices.
Web Interfaces: Browser-based tools for device configuration.

## Slide 37: CLI: Configuration
Ping: Tests connectivity- used to test the reachability of a host on an Internet Protocol network.
IPConfig: Displays network configurations. Used for finding the IP address and default gateway of your network.
NETSTAT: Shows network connections and ports.- displays network connections for Transmission Control Protocol, routing tables, and a number of network interface and network protocol statistics.
NSLOOKUP: nslookup is a network administration command-line tool for querying the Domain Name System to obtain the mapping between domain name and IP address, or other DNS records.
Traceroute and tracert: Shows path packets take. - displays possible routes and transit delays of packets across an Internet Protocol network. The command reports the round-trip times of the packets received from each successive host along the route to a destination.

## Slide 38: CLI: Configuration Ctnd
The ARP: Address Resolution Protocol command is used to access the mapping structure of IP addresses to the MAC address. This provides us with a better understanding of the transmission of packets in the network channel.
getmac (get mac address): This command returns the MAC address from all the network cards on a system.
HOSTNAME: For Linux users, hostname is a commonly used networking command in cmd that helps set and view the hostname registered to a system. HostName. The Windows HostName network command will simply display the current name of your Windows computer.
Netsh: or network shell, is a command-line utility included in Microsoft's Windows NT line of operating systems beginning with Windows 2000. It allows local or remote configuration of network devices such as the interface.

## Slide 39: Protocols

## Slide 40: Network Protocols
A network protocol: is a set of rules outlining how connected devices communicate across a network to exchange information easily and safely.
Protocols ensure that devices on a network can communicate with each other, regardless of differences in their internal processes, hardware, or software.
They play a crucial role in enabling reliable and efficient communication between devices, such as computers, routers, switches, and servers, in local or wide-area networks (LANs or WANs) and across the internet.

## Slide 41: Network Protocols
TCP/UDP: Data transport control
  TCP/IP (Transmission Control Protocol/Internet Protocol): Foundation of the Internet. Provides reliable, ordered, and error-checked delivery.
  UDP (User Datagram Protocol): Lightweight, connectionless protocol. Faster but less reliable.
HTTP/HTTPS (Hypertext Transfer Protocol/Secure): Protocols for web communication; HTTPS includes SSL/TLS for security.
FTP (File Transfer Protocol): Used for transferring files between systems.
SMTP (Simple Mail Transfer Protocol): Protocol for sending emails.
DNS (Domain Name System): Translates domain names to IP addresses.
SNMP (Simple Network Management Protocol): Network Management Manages and monitors network devices.

## Slide 42: Addressing
Addressing in computer networks refers to the methods and schemes used to uniquely identify devices, nodes, or hosts on a network.
Addressing is crucial for ensuring that data packets are transmitted accurately from a source to a destination across a network.
It enables devices to locate and communicate with each other on both local and wide-area networks.

## Slide 43: IP Addressing
An IP Address is a unique identifier assigned to each device on a network.
Types
  IPv4 – 32-bit address (e.g., 192.168.1.1)
  IPv6 – 128-bit address (e.g., 2001:0db8::1)
Subnetting: Dividing a network into smaller segments.

## Slide 50: Network Maintenance and Troubleshooting

## Slide 51: Maintenance
Regular Updates: Keeping software and firmware up to date.
Monitoring: Using tools to monitor network performance and detect issues.
Backup: Regularly backing up network configurations and data.

## Slide 52: Troubleshooting Steps
1. Identify the Problem: Gathering information and defining the issue.
2. Develop a Hypothesis: Formulating possible causes.
3. Test the Hypothesis: Trying solutions to see if they resolve the issue.
4. Document: Recording the problem and solution for future reference.

## Slide 53: Making Network Cables (Crossed, Straight)

## Slide 54: Tools and Materials
Tools: Crimping tool, cable tester, wire stripper.
Materials: Twisted pair cables (Cat5e, Cat6), RJ45 connectors.

## Slide 55: Straight-Through Cables
Usage: Connecting different types of devices (e.g., computer to switch).
Wiring: Both ends use the same wiring standard (either T568A or T568B).

## Slide 56: Crossover Cables
Usage: Connecting similar devices (e.g., computer to computer).
Wiring: One end uses T568A and the other end uses T568B.

## Slide 59: VIDEO LINKS
https://youtu.be/Uw8FSXx4dnU
https://youtu.be/NWhoJp8UQpo
https://youtu.be/2OLeNqsNATQ
https://youtu.be/-bQjrDirT6g

## Slide 60: THANK you

## Slide 61: DOWNLOAD
CISCO PACKET TRACER
Download and Install Packet Tracer: Link:
https://www.netacad.com/resources/lab-downloads