## Slide 1: Dynamic vs Static routes

## Slide 2: Statically Learned Routes
Static routes are manually configured and They define an explicit path between two networking devices.
static routes are not automatically updated and must be manually reconfigured if the network topology changes
. The benefits of using static routes include;
  improved security and resource efficiency.
  Static routes use less bandwidth than dynamic routing protocols,
  no CPU cycles are used to calculate and communicate routes.
The main disadvantage to using static routes is the lack of automatic reconfiguration if the network topology changes.

## Slide 3: Statically Learned Routes
There are two common types of static routes in the routing table:
  Static route to a specific network
  Default static route
A static route can be configured to reach a specific remote network.
IPv4 static routes are configured using the ip route network mask {next-hop-ip | exit-intf}global configuration command.
A static route is identified in the routing table with the code ‘S’.

## Slide 4: Statically Learned Routes
A default static route is similar to a default gateway on a host. The default static route specifies the exit point to use when the routing table does not contain a path for the destination network.
A default static route is useful when a router has only one exit point to another router, such as when the router connects to a central router or service provider.
To configure an IPv4 default static route, use the ip route 0.0.0.0 0.0.0.0 {exit-intf | next-hop-ip} global configuration command.

## Slide 5: Statically Learned Routes

## Slide 6: Dynamic Routing Protocols
Dynamic routing protocols are used by routers to share information about the reachability and status of remote networks.
Dynamic routing protocols perform several activities, including network discovery and maintaining routing tables.

## Slide 7: IPv6 Routing Protocols
As shown in the figure, the router can support dynamic IPv6 routing protocols including:
RIPng (RIP next generation)
OSPFv3
EIGRP for IPv6
Support for dynamic IPv6 routing protocols is dependent on hardware and IOS version. Most of the modifications in the routing protocols are to support the longer IPv6 addresses and different header structures.
To enable IPv6 routers to forward traffic, you must configure the ipv6 unicast-routing global configuration command.

## Slide 8: Dynamic Routing Protocols
A router running a dynamic routing protocol also determines a new best path if the initial path becomes unusable (or if the topology changes).
dynamic routing protocols advantage over static routes are:
  Routers that use dynamic routing protocols automatically share routing information with other routers
  It compensates for any topology changes without involving the network administrator.
Cisco ISR routers can support a variety of dynamic IPv4 routing protocols including:
  EIGRP - Enhanced Interior Gateway Routing Protocol
  OSPF - Open Shortest Path First
  IS-IS - Intermediate System-to-Intermediate System
  RIP - Routing Information Protocol
To determine which routing protocols are supported by the IOS, use the router ? command in global configuration.

## Slide 9: How to configure Dynamic Routing Protocols specifically RIPv2
To configure an IPv4 Rip route, use the router rip in global configuration command.
Specify the rip version as by default its version 1, so specify by using version 2
Network {ip address advertised}

## Slide 10: ASSIGNMENT
ON MUBSEP