## Slide 1: Introduction to Networks and Networking Concepts

## Slide 2: Learning Objectives
Understand basic networked communications and services
Identify essential network components
Describe the benefits of networking
Understand and compare peer-to-peer and server-based networks
Apply your knowledge when selecting an appropriate network type for small business use
Suggest possible redesigns for a small but expanding network

## Slide 3: What is Networking?
Connecting computers to share information and resources
Complex and varied technology
Many choices for physical connections and related software

## Slide 4: Networking Fundamentals
As simple as two computers connected with a cable that can transmit data
Allows users to share data quickly and efficiently
Access to shared peripheral devices such as printers, scanners, and fax machines

## Slide 5: Advantages of Networks
Allow groups of users to exchange information and share data
Allow easy and efficient communication among individuals, including electronic mail (e-mail)
Device sharing can reduce costs

## Slide 6: Standalone Computer and a “Sneakernet”
Standalone computer
  Single computer not attached to a network
  Cannot match power and convenience of network
“Sneakernet”
  Passing floppy disk from machine to machine
  Old alternative to networking

## Slide 7: Sharing Resources on a Simple Network
Networking computers allows them to:
  Share data
  Access shared printer and other equipment

## Slide 8: Local Area Networks (LANs) and Internetworks
Early networks – custom-built, expensive, severe restrictions
Early Ethernet – no more than 30 users with total span of 607 feet
Local area network (LAN) – works within limited geographic area
  Building block for constructing larger networks, called internetworks
Internetwork – network 100 or more computers at distances in excess of 1000 feet

## Slide 9: Wide Area Networks (WANs) and the Internet
Wide area network (WAN) – spans distances measured in miles; links two or more separate LANS
Metropolitan area network (MAN) – uses WAN technology to interconnect LANs within a specific geographic region
Internet – global WAN internetwork; includes millions of machines and users worldwide

## Slide 10: A Networking Lexicon
Must understand specialized networking vocabulary, including
  Server — shares resources across network, typically with more central processing unit (CPU) power and storage capacity than other computers
  Client — accesses shared resources
  Request-response — client requests information; server responds by providing information
  Client-server relationship — client makes a request to the server, and the server responds with requested data
  Peer-to-peer — computers share and request resources from one another

## Slide 11: Client-Server Relationship

## Slide 12: Network Medium Carries Network Messages
Computers share access to common network medium that carries signals from one computer to another
  Medium may be physical cable, such as twisted pair, coaxial, or fiber-optic
  Medium may be wireless
Physical interface to medium is usually network interface card (NIC) or network adapter
Kind of medium dictates type of connector and limits number and type of devices as well as distance a single LAN can span

## Slide 13: Network Protocols
Network protocols – a common set of rules
Define how to interpret signals, identify individual computers, initiate and end networked communication, and manage information exchange across network medium
Include TCP/IP, NetBEUI, IPX/SPX, and NWLink

## Slide 14: Network Software
Network software issues requests and responses
Network operating system (NOS) controls which computers and users access network resources
  Include both client and server components
  Popular NOSs include Windows Server 2003, Windows XP, Windows 2000, Windows NT, and Novell NetWare
Network applications access the network
  Include e-mail programs, Web browsers, and network-oriented utilities

## Slide 15: Network Services
Services include file and print services, file-sharing, e-mail, and other capabilities
Network communications are layered
Network applications use NOS or client networking software to get network protocol to access medium
Medium exchanges information with other computers
Figure 1-4 shows layers of networking process

## Slide 16: Layers of the Networking Process

## Slide 17: Network Types
Two major types of networks
  Peer-to-peer
  Client/Server (also called server-based)

## Slide 18: Peer-to-Peer Networking
Peers with no centralized control over shared resources
Can share resources with any other computer on network
No computer has higher access priority
No computer has more responsibility to provide or shared resources
Figure 1-5 shows typical peer-to-peer network

## Slide 19: Peer-to-Peer Network

## Slide 20: Peer-to-Peer Networking Advantages
Easy to install and configure
No dedicated server
Users control own shared resources
Inexpensive to purchase and operate
No additional equipment or software
No dedicated administrators
Works best with 10 or fewer users

## Slide 21: Peer-to-Peer Networking Disadvantages
Security applies to single resource at a time
Users may have many different passwords
Must back up each machine individually
Machine sharing resources may suffer reduced performance
No centralized organization scheme to locate or control access to data
Does not usually work well with more than 10 users

## Slide 22: Server-Based Networks
Server responds to client requests
Next slide shows a typical server-based network
Provide centralized control over resources
Servers require faster CPUs, more memory, larger disk drives, and extra peripherals such as tape drives
May be dedicated, handling only requests from client communities

## Slide 23: Server-Based Networks (continued)

## Slide 24: Server-Based Networks (continued)
One or more servers may do centralized verification of user accounts and passwords
Novell and Windows servers use a directory service
  Checks account names and passwords against database
  Manage shared resources
  Windows 2000/2003 calls it Active Directory
  Novell NetWare calls it Novell Directory Services (NDS)

## Slide 25: Server-Based Networks (continued)
Easier to scale
May handle thousands of users

## Slide 26: Server-Based Networking Advantages
Simplifies network administration
Centralizes user accounts, security, and access controls
More powerful equipment
More efficient access to network resources
Single password for network logon
Best choice for networks with 10 or more users or network with heavily-used resources

## Slide 27: Server-Based Networking Disadvantages
At worst, server failure renders network unusable
At least, server failure causes loss of network resources
More expensive
Requires expert staff to handle complex server software
Requires dedicated hardware and specialized software

## Slide 28: Storage-Area Networks (SANs)
Uses high-speed network links between servers in enterprise and centralized storage systems
Data and applications reside on centralized storage
Sideband link connecting SAN components is completely separate from network that links clients and servers
Figure 1-7 shows typical storage area network

## Slide 29: Storage-Area Networks (continued)

## Slide 30: Storage-Area Networks (continued)
Provide centralized control over network storage
Much more expensive than conventional storage

## Slide 31: Storage-Area Networks (continued)
Offer many advantages, including:
  Fast access to SAN storage
  Backups from single location
  Fastest, more reliable storage subsystems, including hot-swappable power supplies and disk drives
  Extra level of security and access control
  Easier to increase storage capacity

## Slide 32: Wireless Personal Area Networks (WPANs)
Short-range networking technology used to connect personal computing and communication devices
Include devices that user wears or comes in close contact with
  Cell phones, pagers, personal digital assistants (PDAs), and even watches
Short range transmission, typically 10 meters or less
Use secure access method

## Slide 33: Wireless Personal Area Networks (WPANs) (continued)
No single standard exists for PANs
Ericcson developed short-range networking technology called Bluetooth
Emerging standard is IEEE 802.15, dubbed wireless personal area network (WPAN)

## Slide 34: Hybrid Networks
Combination networks
Workstations function simultaneously as peers on a peer-to-peer network and as clients on server-based networks
Modern operating systems can function both as peers and as clients
  Windows Server 2003, Windows 2000, Windows XP

## Slide 35: Server Hardware Requirements
Equip server with fastest CPU, as much RAM as possible, as much disk space as it will hold, and fastest NIC available
  Windows 2000 Server and Windows Server 2003 handle up to 32 CPUs in single system
  Specialized versions handle 64 or more processors

## Slide 36: Application Servers
Supply server side of client/server applications
Provide processing service and handle requests for file or print services
  Example: database server supplies query-processing and data-analysis facilities; repository for huge amounts of data within database

## Slide 37: Communication Servers
Allow users outside network to access network’s resources (inbound communications)
Sometimes permit users on network to access resources outside network (outbound communications)
Users may dial into network with modem
  Example: Windows 2000/2003 Server includes Remote Routing and Access Server (RRAS)

## Slide 38: Domain Controllers/ Directory Servers
Let users locate, store, and secure information about network and its resources
  Windows Servers combine computers, users, groups, and resources into logical domains

## Slide 39: Domain Controllers/ Directory Servers (continued)
Domain controller or directory server handles logon service
  By logging onto domain, user has access to all permitted resources and information
  Windows 2000/2003 Server and NetWare 4.x and newer versions include software to let server function as domain controller or directory server
  Linux directory service is called NIS

## Slide 40: Fax Servers
Manage fax traffic on network
Receive incoming faxes via telephone
Distribute faxes to recipients
Collect outgoing faxes to send via telephone
Must have at least one fax modem interface
Third-party vendors supply software to create Windows, NetWare, or Linux-based fax servers

## Slide 41: File and Print Servers
Provide basic network file storage and retrieval
Provide access to networked printers
Users run applications locally but keep data files on server and print hard-copies
Any Windows, NetWare, or Linux server can act as file and print server

## Slide 42: Mail Servers
Handle e-mail messages
Provide “store and forward” services
Hold incoming e-mail messages until users access them
Can hold outgoing e-mail messages until forwarded to their destinations
Microsoft Exchange Server runs on Windows 2000/2003; NetWare and Linux use other e-mail server programs

## Slide 43: Web Servers
Has gained popularity faster than any other single service
Many companies use WWW and TCP/IP protocol to distribute information via the Internet
May set up Web server to handle Internet traffic
  Windows .NET Server and Windows 2000 Server include Internet Information Server (IIS), a complete Web server
  NetWare versions 4.x and 5.x include Netscape Web server
  Apache Web server is available free for Linux

## Slide 44: Web-Based Networks
Internet and the WWW are becoming part of our everyday lives
Most computers are connected to Internet
Handheld devices such as cell phones and PDAs are connected through wireless communications
Cable modems and high-speed connections are common at work and home
New technologies such as Microsoft .NET will further integrate Web into our lives so that the Web is the network

## Slide 45: .NET Computing
Uses Web to deliver information and applications; allows devices to communicate and share data
Permits handheld computers to transfer information to and from network server using the Web
Allows transfer of information with unprecedented ease and convenience

## Slide 46: Web-Enabled Devices
WPANs include many Web-enabled devices that can transmit information via the Internet
Other devices are becoming Web-enabled such as automobiles with wireless navigation systems
Networking paradigm is shifting from clients and servers to Web-enabled or not Web-enabled
  Client will be any Web-enabled device that needs information
  Server will be any Web-enabled device that provides information

## Slide 47: Selecting the Right Type of Network
Choose peer-to-peer networking only if all these conditions are true:
  Network includes no more than 10 users
  All networked machines are close enough to form a single LAN
  Budget considerations are paramount
  No specialized servers are needed

## Slide 48: Selecting the Right Type of Network (continued)
Choose server-based network when one or more of the following conditions is true:
  More than 10 users share network access
  Centralized control, security, resource management, or backup is desirable
  Need specialized servers
  Heavy demands for network resources
  Use Internetwork or require WAN access

## Slide 49: Selecting the Right Type of Network (continued)
Consider future growth
  Even if peer-to-peer network serves current needs, may be best to implement server-based network

## Slide 50: Chapter Summary
Basic elements of networks include networking medium (cabling) and computers with physical interface (network adapter) to medium
Computers must also have network protocol and network software to send and receive messages across network
Network services include file sharing, printing, e-mail, and other messaging services

## Slide 51: Chapter Summary (continued)
Four basic types of networks include peer-to-peer, server-based, storage-area, and hybrid
Wireless personal area network (WPAN) is new kind of network limited to small area around a person
Major criteria for selecting network type include budget, number of users, types of applications or network services, and requirements for centralized administration and control

## Slide 52: Chapter Summary (continued)
Servers require specialized hardware and software
Servers may take specific roles, serving as file and print servers, fax servers, e-mail servers, application servers, and so on