## Slide 1: TOPIC 2: PC COMPONENTS

## Slide 2: Motherboard
Function: The main circuit board that holds the CPU, memory, and other essential components and allows them to communicate.

## Slide 5: Motherboards
1. AT (Advanced Technology):
Older form factor, now obsolete, Large size, limited connectivity.
2. ATX (Advanced Technology Extended):
The most common form factor, Standardized size: 305 x 244 mm, Good expandability and cooling.

## Slide 6
3. BTX (Balanced Technology Extended):
Improved airflow and cooling, Less common than ATX.
4. Micro ATX:
Smaller than ATX: 244 x 244 mm, Fewer expansion slots but compatible with ATX cases.
5. NLX (New Low Profile Extended):
Designed for slimline cases, Not widely used today.

## Slide 8: Input Devices
Mouse
Types: Optical, laser, mechanical.
Functions: Pointing, clicking, scrolling.
Keyboard
Types: Membrane, mechanical.
Layout: QWERTY, AZERTY.
Features: Function keys, multimedia keys, ergonomic designs.

## Slide 9: Multimedia Input Devices
Game Controllers: Joysticks, gamepads.
Audio Input: Microphones, MIDI devices.

## Slide 11: Ports:
Function: Allow the connection of peripheral devices to the computer.
Types:
  USB (Universal Serial Bus): Used for connecting a wide range of devices like keyboards, mice, printers, and external storage.
  HDMI (High-Definition Multimedia Interface): Transmits video and audio from the computer to an external display or TV.
  Ethernet Port: For wired network connections using an Ethernet cable.

## Slide 12: Ports and Cables
1. USB (Universal Serial Bus)
Versions: USB 1.0/1.1, 2.0, 3.0, 3.1, 3.2, 4.0.
Connectors: Type-A, Type-B, Micro-USB, USB-C.
Uses: Data transfer, power supply.

## Slide 14
2. Parallel Ports
Characteristics: Used for printers, older technology.
Connectors: 25-pin D-sub connector.
3. Serial Ports
Characteristics: Used for modems, mice, older technology.
Connectors: 9-pin D-sub connector.
4. IEEE 1394 (FireWire)
Versions: 400, 800.
Uses: High-speed data transfer, multimedia devices.

## Slide 18: Buses
a bus is a communication system that transfers data between components inside or between computers.
1. System Bus
Components: Data bus, address bus, control bus.
Function: Connects CPU to RAM and other system components.
2. I/O Buses
ISA (Industry Standard Architecture): Older technology, slower speeds.
PCI (Peripheral Component Interconnect): Widely used for expansion cards.
3. USB: Versatile, hot-swappable, and widely used for peripherals.

## Slide 21
Central Processing Unit and How it Works

## Slide 22: Central Processing Unit (CPU)
Definition: The brain of the computer that performs instructions defined by software.
Function: Executes instructions from software by performing basic arithmetic, logic, control, and input/output operations.

## Slide 23: CPUs
AMD & Intel
AMD: Known for Ryzen and EPYC processors.
Intel: Known for Core, Xeon, and Pentium processors.
CPU Technologies
Multi-core Processors: Multiple processing cores on a single chip.
Hyper-Threading: Simultaneous multi-threading to improve efficiency.
Cache Memory: L1, L2, and L3 caches for faster data access.

## Slide 25: CPU Components
Arithmetic Logic Unit (ALU): Performs arithmetic and logical operations.
Control Unit (CU): Directs operations of the processor by telling the ALU, memory, and I/O devices how to respond to the instructions.
Cache Memory: Small, fast memory located inside or very close to the CPU for quick access to frequently used data.

## Slide 28: How the CPU Works (Step by Step)
Fetch: The CPU gets (fetches) the next instruction from the computer’s memory (RAM).Instructions are stored as binary code (0s and 1s).
Decode: The CPU’s control unit (CU) interprets the instruction. It figures out what needs to be done (e.g., add numbers, compare values, move data).
Execute: The Arithmetic Logic Unit (ALU) carries out the actual work: Arithmetic (addition, subtraction, multiplication, division) Logic (AND, OR, NOT, comparisons). If the task involves moving data, the CPU handles that too.
Store (Write Back): The result of the instruction is sent back to RAM, cache, or a register (a small, super-fast storage inside the CPU) for future use.
This cycle is called the Fetch–Decode–Execute cycle, and it happens billions of times per second.

## Slide 29: Key CPU Components
Control Unit (CU): Directs data flow, tells other parts what to do.
Arithmetic Logic Unit (ALU): Performs calculations and logical comparisons.
Registers: Tiny, high-speed memory inside the CPU for immediate data.
Cache: Very fast memory inside or near the CPU to store frequently used data.
Clock: Synchronizes all operations (measured in GHz – billions of cycles per second).

## Slide 30: PC Memory
Primary storage or memory: Is where the data and programs that are currently in operation or being accessed are stored during use.
Instructions and data are held in main memory, which is divided into millions of individually-addressable storage units called bytes.
One byte can hold one character, or it can be used to hold a code representing, for example, a tiny part of a picture, a sound, or part of a computer program instruction.
One byte has bits

## Slide 31: Memory Size
The total number of bytes in main memory is referred to as the computer’s memory size. Computer memory sizes are measured as follows:
1 Byte= 8bits
1 Kilobyte (Kb) = 1000 bytes (to be exact, 1024 bytes) [1000 bytes form = 1 Kilobyte]
1 Megabyte (Mb)= 1,000,000 (1 million) bytes [1000 kilobytes =1 Megabyte(MB)]
1 Gigabyte (Gb) = 1,000,000,000 (1 billion) bytes [1000 MB= 1 Gigabyte(GB)]
1 Terabyte (Tb) = 1,000,000,000,000 (1 trillion) bytes [1000 GB= 1 Terabyte(TB)]

## Slide 32
Main memory consists of a number of storage locations, each of which is identified by a unique address
The ability of the CPU to identify each location is known as its addressability
Each location stores a word i.e. the number of bits that can be processed by the CPU in a single operation. Word length may be typically 16, 24, 32 etc

## Slide 33: RAM)
Memory (RAM): Temporary storage used by the CPU to store data and instructions during processing.
Function: Stores data temporarily for quick access by the CPU.

## Slide 34: RAM TYPES
DRAM (Dynamic RAM):
Most common type of memory found in computers.
Volatile, needs a constant refresh, Common in PCs.
2. SRAM (Static RAM):
Faster and more expensive than DRAM, no refresh needed , used for cache memory.
3. SDRAM (Synchronous DRAM): Synchronized with the system clock.
Includes DDR (Double Data Rate) versions (DDR, DDR2, DDR3, DDR4, DDR5).

## Slide 36: RAM Note
Motherboards are designed to support specific types of RAM.
You should always check which types of memory can be fitted before supplying or installing upgrades.
The memory must be equal to or faster than the motherboard clock speed.

## Slide 37: Read Only Memory (ROM)
Non-volatile, with contents permanently attached to the memory chip at the manufacturing stage
Used for example to hold the bootstrap loader, the program which runs as soon as the computer is switched on and instructs it to load the operating system from disk into memory.

## Slide 38: ROM Types
1.Programmable read-only memory,(PROM):
A memory chip on which data can be written only once.
Once a program has been written onto a PROM, it remains there forever. Unlike RAM, PROMs retain their contents when the computer is turned off..
To write data onto a PROM chip, you need a special device called a PROM programmer or PROM burner. The process of programming a PROM is sometimes called burning the PROM.

## Slide 39
2.An EPROM (Erasable programmable read-only memory)
is a special type of PROM that can be erased by exposing it to ultraviolet light. Once it is erased, it can be reprogrammed. An EEPROM is similar to a PROM, but requires only electricity to be erased.

## Slide 40: Storage Device
1. Hard Disk Drives (HDD)
Installation: Secure in case, connect power and data cables.
Configuration: BIOS/UEFI recognition, partitioning, formatting.
2. Solid State Drives (SSD)
Installation: Similar to HDDs, often mounted differently.
Configuration: BIOS/UEFI settings, partitioning, formatting.

## Slide 41: Storage Device Cont’d
3. Floppy Drives
Installation: Secure in case, connect power and data cables.
Configuration: BIOS recognition.
4. CD-ROM Drives
Installation: Secure in case, connect power and data cables.
Configuration: BIOS/UEFI settings.

## Slide 43: Display Devices
1. Projectors
Types: LCD, DLP.
Uses: Presentations, media display.
2. CRT (Cathode Ray Tube) Monitors
Characteristics: Bulky, high power consumption, now obsolete.
3. LCD (Liquid Crystal Display) Monitors
Characteristics: Slim, energy-efficient, widely used.
Types: TN, IPS, VA panels.

## Slide 45: Installation and Configuration of Personal Computer Components
Installation
Components: CPU, RAM, GPU, storage devices.
Software: Operating system, drivers.
Configuration
BIOS/UEFI Settings: Boot order, hardware recognition.
Operating System Configuration: Driver installation, and system updates.

## Slide 46: Identifying Personal Computer Components
Major Components
Motherboard: Main circuit board.
CPU: Central processing unit.
RAM: Random access memory.
Storage Devices: HDD, SSD.
Power Supply: Provides power to all components.
GPU: Graphics Processing Unit.
Cooling: Fans, heat sinks, liquid cooling.

## Slide 48: Peripheral Components
Monitor: Display output.
Keyboard and Mouse: Input devices.
Printers and Scanners: Output and input devices.

## Slide 50
Assembling & Disassembling of Computer Systems

## Slide 51: Disassembling a Computer System
1. Preparation:
Ensure the system is powered off and unplugged.
Ground yourself with an anti-static wrist strap.

## Slide 52: Disassembling Steps Cont’d
Open the Case: Remove screws and panels.
Disconnect Power: Unplug power cables from all components.
Remove Components: Sequentially remove the GPU, storage devices, RAM, CPU cooler, CPU, and finally the motherboard.
Organize Parts: Keep screws and small parts in labelled containers for reassembly.

## Slide 53: Assembling a Computer System
1. Preparation:
Gather all components: case, motherboard, CPU, RAM, storage, power supply, GPU, cooling, peripherals.
Ensure a clean, static-free workspace.
Have tools ready: screwdrivers, thermal paste, anti-static wrist strap.

## Slide 54: Assembling Steps Cont’d
  Install the Power Supply: Secure the power supply in the case.
  Mount the Motherboard: Place standoffs in the case, align the motherboard, and secure it.
  Install the CPU: Open the CPU socket, place the CPU, close the socket, and apply thermal paste.
  Attach the CPU Cooler: Mount the cooler and connect the fan to the motherboard.
  Install RAM: Insert RAM modules into the motherboard slots.

## Slide 55: Assembling Steps Cont’d
  Install Storage Devices: Secure HDDs/SSDs and connect power and data cables.
  Install the GPU: Place the GPU in the appropriate PCIe slot and secure it.
  Connect Power Cables: Attach power cables to the motherboard, GPU, storage devices, and peripherals.
  Connect Front Panel Cables: Connect USB, audio, and power/reset buttons to the motherboard.
  Final Checks: Ensure all connections are secure, then close the case.

## Slide 56: END