## Slide 1: BIOS, CMOS & System resources
Topic 6
Notes: NOTE:
To change the image on this slide, select the picture and delete it. Then click the Pictures icon in the placeholder to insert your own image.

## Slide 2: Introduction
When a computer starts, it doesn’t go straight into Windows, Linux, or macOS.
First, the system runs firmware instructions stored in a chip.
These instructions check hardware, configure devices, and load the operating system.
BIOS (Basic Input/Output System) and CMOS (Complementary Metal-Oxide Semiconductor) are key players in this process.

## Slide 3: What is BIOS?
BIOS = Basic Input/Output System.
A firmware program stored on a ROM/Flash memory chip on the motherboard.
Provides the first code executed when the computer is powered on

## Slide 5: Functions of BIOS
1. Power-On Self-Test (POST):
Checks CPU, RAM, keyboard, storage, etc.
Detects hardware errors before booting.
2. Bootstrap Loader:
Locates and loads the operating system from storage (e.g., HDD, SSD, USB).
3. BIOS Drivers:
Provide basic communication between OS and hardware (keyboard, monitor, storage).
4. BIOS Setup Utility:
Interface where users configure system settings (boot order, CPU settings, security).

## Slide 6: BIOS Boot Process
Power is turned on.
BIOS runs POST (tests CPU, RAM, and devices).
BIOS checks CMOS settings for configuration.
BIOS locates boot device (e.g., SSD, HDD).
Loads the bootloader → Operating System starts.

## Slide 8: What is CMOS?
CMOS = Complementary Metal-Oxide Semiconductor.
A small memory chip that stores BIOS settings.
Powered by a small CMOS battery (coin-cell battery on the motherboard).

## Slide 9: Role of CMOS
1. Stores system configuration:
Date and Time.
Boot sequence.
CPU and memory settings.
Hardware configuration (hard drives, optical drives, etc.).
Security settings (passwords).
2. Without CMOS battery:
Settings reset to default when the computer is turned off.

## Slide 10
Aspect | BIOS | CMOS
Nature | Firmware (software on a chip) | Small memory chip (hardware + battery)
Location | ROM/Flash chip on motherboard | Battery-powered RAM chip
Function | Executes POST, loads OS | Stores configuration settings
Volatility | Non-volatile (stays even w/out power) | Volatile (needs battery to retain data)

## Slide 11: Accessing BIOS/CMOS Setup
Press a key during startup (varies by manufacturer):
DEL, F2, F10, ESC,F12 (common keys).
Brings up BIOS Setup Utility.

## Slide 12: Common BIOS/CMOS Settings
Boot Order: Priority sequence for boot devices (SSD, HDD, USB, DVD).
System Date/Time: Configured here and stored in CMOS.
Hardware Configuration: Enable/disable onboard devices (sound, LAN, USB ports).
Virtualization Support: Enable (VT-x on Intel, AMD-V on AMD) for running virtual machines.
Security: Set BIOS/UEFI passwords (supervisor/user) and Secure Boot options.

## Slide 14: Common CMOS/BIOS Issues
1. Dead CMOS Battery:
Symptoms: Wrong time/date, reset settings.
2. Corrupted BIOS:
System won’t boot.
3. Incorrect BIOS Settings:
Boot failure or hardware not recognized.
Solutions:
Replace CMOS battery,
Reset BIOS to default,
Update/flash BIOS if necessary.

## Slide 15: Legacy BIOS Vs UEFI
Legacy BIOS
  Older type of BIOS.
  Limited to 16-bit code execution and 1 MB of addressable memory.
UEFI (Unified Extensible Firmware Interface)
  Modern BIOS replacement.
  More advanced than traditional BIOS
  Supports 32-bit and 64-bit code execution.
  Supports larger hard drives, faster boot, graphical interface.
  Backward compatible with BIOS.

## Slide 17: Discussion Questions
What would happen if the CMOS battery dies?
Why is BIOS considered firmware, not software?
How does UEFI improve upon traditional BIOS?
Describe a situation where you might need to enter BIOS/CMOS setup.

## Slide 18: System Resources
System resources are the hardware and software components that an operating system (OS) manages to ensure efficient functioning of the computer.
Examples:
CPU time, Memory, Input/Output devices, files/data, Networks etc

## Slide 19: Importance of System Resources
They enable smooth functioning of applications.
Efficient allocation thus prevents:
  Conflicts (two devices using same resource).
  Performance bottlenecks.
Critical for multitasking and resource sharing.

## Slide 20: Types of System Resources
Processor (CPU time)
Memory (RAM, cache, virtual memory)
Storage devices (Hard drive, SSD)
Input/Output (I/O) devices
Files & Data
Network resources

## Slide 21: 1. CPU (Processor Time)
Role: Executes instructions and performs computations.
Resource management:
  Scheduling – decides which process gets CPU and for how long.
  Techniques: Round Robin, Priority Scheduling, First-Come-First-Serve.
Issues: Starvation, deadlock.

## Slide 22: 2. Memory Resources
Primary memory (RAM): fast, volatile.
Cache memory: high-speed, between CPU & RAM.
Virtual memory: extends RAM using disk space.
OS tasks:
  Allocation and deallocation.
  Memory protection (processes can’t access others’ memory).
  Swapping (moving processes in and out).

## Slide 23: 3. Storage Resources
Types: HDD, SSD, optical disks.
Functions: Store operating system, applications, and user data.
OS management:
  File system organization (e.g., NTFS, FAT32, EXT4).
  Access permissions.
  Disk scheduling (FCFS, SSTF, SCAN).

## Slide 24: 4. Input/Output (I/O) Resources
Devices: Keyboard, mouse, monitor, printer, scanners, USBs.
Managed through:
  Device drivers (software that communicates with hardware).
  Interrupts (signals to CPU from I/O device).
Challenges: Speed mismatch between CPU and I/O devices.

## Slide 25: 5. File and Data Resources
Files: Named collection of data stored on disk.
Resource management by OS:
  File naming and structure.
  Access control (read/write/execute permissions).
  Space allocation.
Example: Multiple processes accessing the same file.

## Slide 26: 6. Network Resources
Includes: Bandwidth, IP addresses, ports, and sockets.
Managed by: Network protocols (TCP/IP).
Resource sharing: Printers, storage, internet.
Issues: Latency, congestion, security.

## Slide 27: Resource Conflicts
Occur when multiple processes compete for limited resources.
Types:
  Deadlock: processes wait indefinitely for resources.
  Starvation: process never gets resources.
Solutions:
  Deadlock prevention, detection, and recovery.
  Fair scheduling algorithms.

## Slide 28: Managing System Resources
Methods:
  Plug and Play (PnP): OS auto-assigns resources.
  Device Manager (Windows): Configure or troubleshoot conflicts.
  BIOS/UEFI Settings: Manually assign IRQs or DMA.
Modern OSs reduce manual conflicts.

## Slide 29: Resource Monitoring Tools
Purpose: Monitor CPU usage, memory consumption, I/O activity, network traffic.
Examples in Windows: Task Manager, Resource Monitor.
Examples in Linux: top, htop, vmstat.

## Slide 30: Practical Example: Configuring BIOS/CMOS Settings
Accessing BIOS: Restart your computer and press the designated key (e.g., F2, Del, Esc) to enter BIOS setup.
Setting System Time and Date:
  Navigate to the "System Time" and "System Date" fields.
  Adjust the values using the arrow keys and Enter.
Configuring Boot Order:
  Navigate to the "Boot" menu
  4. Use Device Manager: Open Device Manager in Windows, expand the device categories, and view the resource settings for each device.

## Slide 31: Reading Assignment
Research and prepare a short report on UEFI vs BIOS.
Include advantages, disadvantages of each

## Slide 32: END