## Slide 1: Networking Fundamentals & Terminologies
Topic 1
Notes: NOTE:
To change the image on this slide, select the picture and delete it. Then click the Pictures icon in the placeholder to insert your own image.

## Slide 2: Basic Networking Concepts
Definition:
Networking: involves connecting computers and other devices to share resources such as data, applications, and hardware like printers.
It allows users to communicate and collaborate effectively through data exchange.

## Slide 3: Key Networking Terms
Node: Any device connected to a network (e.g., computer, printer).
Host: A node that provides resources or services to other nodes.
Protocol: A set of rules for communication between devices (e.g., TCP/IP).

## Slide 5: Ctn’d
IP Address: A unique identifier assigned to each device on a network.
MAC Address: A hardware identifier unique to a network interface card (NIC).
Bandwidth: The data transfer capacity of a network, typically measured in Mbps or Gbps.
Latency: The delay in data transmission across the network.

## Slide 6: Benefits of Networking
Resource Sharing: Enables shared use of hardware, software, and data.
Communication: Facilitates email, messaging, and video conferencing.
Centralized Management: Allows network administrators to manage resources efficiently.
Scalability: Easier to expand and integrate additional devices.
Cost Efficiency: Reduces expenses by sharing resources and infrastructure.

## Slide 7: Types of Networks by Functionality
1. Personal Area Network (PAN):
  Used for personal devices like smartphones, tablets, and laptops.
  Example: Bluetooth connections between a smartphone and a headset.
2. Home Network:
  Connects devices within a home for internet access and resource sharing.
  Example: Wi-Fi routers connecting smart TVs, laptops, and phones.
3. Enterprise Network:
  Designed for businesses to support high traffic, security, and scalability.
  Example: Office LANs with servers hosting enterprise applications like ERP systems.

## Slide 8: Types of Networks
1. Peer-to-Peer Networks (P2P):
  Every device has equal status, and resources are shared directly between devices.
  Peers with no centralized control over shared resources
  Can share resources with any other computer on network
  No computer has higher access priority
  No computer has more responsibility to provide or shared resources
  Best suited for small-scale networks (e.g., home or small office).
  Example: File sharing using Windows Workgroup or BitTorrent.

## Slide 9
2. Client-Server Networks:
  A central server provides resources and services to client devices.
  Common in larger organizations due to better security and centralized management.
  Example: Gmail services hosted on Google servers.

## Slide 10: Classification of Networks by Scale
LAN (Local Area Network):
  Covers a small geographical area (e.g., an office, school).
  Typically uses Ethernet technology and wired or wireless connections.
  Example: A school computer lab.

## Slide 11
2. MAN (Metropolitan Area Network):
  Spans a city or campus, connecting multiple LANs.
  Example: A university campus network interconnecting various buildings.

## Slide 12
3. WAN (Wide Area Network):
  Covers large geographical areas, such as countries or continents.
  Uses technologies like MPLS, satellite links, and leased lines.
  Example: The Internet.

## Slide 13: Network Topologies
Network topology refers to the arrangement of devices and communication links in a network.

## Slide 14: Types of Topologies
Bus Topology
  All devices connect to a single central cable (bus).
  Advantages: Cost-effective, easy to set up.
  Disadvantages: Difficult to troubleshoot; failure in the central cable affects the entire network.
  Example: Early Ethernet networks used a bus topology.

## Slide 15
2. Star Topology
  Devices connect to a central hub or switch.
  Advantages: Easy to add/remove devices; failure of one device doesn’t affect others.
  Disadvantages: Hub failure disrupts the entire network.
  Example: Most modern home and office networks.

## Slide 16
3. Ring Topology
  Devices connect in a circular fashion, forming a closed loop.
  Advantages: Equal access to resources; predictable performance.
  Disadvantages: Failure of one device can disrupt the entire network.
  Example: Token Ring networks.

## Slide 17
4. Mesh Topology
  Devices are interconnected, with multiple paths between nodes.
  Advantages: High redundancy and reliability.
  Disadvantages: Expensive and complex to implement.
  Example: Used in military communication systems.

## Slide 18
5. Hybrid Topology
  Combines features of multiple topologies.
  Example: A star-bus network used in large organizations.

## Slide 19: Networking Terminologies
Must understand specialized networking vocabulary, including
  Server — shares resources across network, typically with more central processing unit (CPU) power and storage capacity than other computers
  Client — accesses shared resources
  Request-response — client requests information; server responds by providing information
  Client-server relationship — client makes a request to the server, and the server responds with requested data
  Peer-to-peer — computers share and request resources from one another

## Slide 20: Client-Server Relationship

## Slide 21: Network Services
Services include file and print services, file-sharing, e-mail, and other capabilities
Network communications are layered
Network applications use NOS or client networking software to get network protocol to access medium
Medium exchanges information with other computers

## Slide 22: Network Types
Two major types of networks
  Peer-to-peer
  Client/Server (also called server-based)

## Slide 23: Peer-to-Peer Networking
Peers with no centralized control over shared resources
Can share resources with any other computer on network
No computer has higher access priority
No computer has more responsibility to provide or shared resources
Figure 1-5 shows typical peer-to-peer network

## Slide 24: Peer-to-Peer Network

## Slide 25: Peer-to-Peer Networking Advantages
Easy to install and configure
No dedicated server
Users control own shared resources
Inexpensive to purchase and operate
No additional equipment or software
No dedicated administrators
Works best with 10 or fewer users

## Slide 26: Peer-to-Peer Networking Disadvantages
Security applies to single resource at a time
Users may have many different passwords
Must back up each machine individually
Machine sharing resources may suffer reduced performance
No centralized organization scheme to locate or control access to data
Does not usually work well with more than 10 users

## Slide 27: Server-Based Networks
Server responds to client requests
Next slide shows a typical server-based network
Provide centralized control over resources
Servers require faster CPUs, more memory, larger disk drives, and extra peripherals such as tape drives
May be dedicated, handling only requests from client communities

## Slide 28: Server-Based Networks (continued)

## Slide 29: Server-Based Networks (continued)
One or more servers may do centralized verification of user accounts and passwords
Novell and Windows servers use a directory service
  Checks account names and passwords against database
  Manage shared resources
  Windows 2000/2003 calls it Active Directory
  Novell NetWare calls it Novell Directory Services (NDS)

## Slide 30: Server-Based Networks (continued)
Easier to scale
May handle thousands of users

## Slide 31: Server-Based Networking Advantages
Simplifies network administration
Centralizes user accounts, security, and access controls
More powerful equipment
More efficient access to network resources
Single password for network logon
Best choice for networks with 10 or more users or network with heavily-used resources

## Slide 32: Server-Based Networking Disadvantages
At worst, server failure renders network unusable
At least, server failure causes loss of network resources
More expensive
Requires expert staff to handle complex server software
Requires dedicated hardware and specialized software

## Slide 33: Storage-Area Networks (SANs)
Uses high-speed network links between servers in enterprise and centralized storage systems
Data and applications reside on centralized storage
Sideband link connecting SAN components is completely separate from network that links clients and servers
Figure 1-7 shows typical storage area network

## Slide 34: Storage-Area Networks (continued)

## Slide 35: Storage-Area Networks (continued)
Provide centralized control over network storage
Much more expensive than conventional storage

## Slide 36: Storage-Area Networks (continued)
Offer many advantages, including:
  Fast access to SAN storage
  Backups from single location
  Fastest, more reliable storage subsystems, including hot-swappable power supplies and disk drives
  Extra level of security and access control
  Easier to increase storage capacity

## Slide 37: Wireless Personal Area Networks (WPANs)
Short-range networking technology used to connect personal computing and communication devices
Include devices that user wears or comes in close contact with
  Cell phones, pagers, personal digital assistants (PDAs), and even watches
Short range transmission, typically 10 meters or less
Use secure access method

## Slide 38: Wireless Personal Area Networks (WPANs) (continued)
No single standard exists for PANs
Ericcson developed short-range networking technology called Bluetooth
Emerging standard is IEEE 802.15, dubbed wireless personal area network (WPAN)

## Slide 39: Hybrid Networks
Combination networks
Workstations function simultaneously as peers on a peer-to-peer network and as clients on server-based networks
Modern operating systems can function both as peers and as clients
  Windows Server 2003, Windows 2000, Windows XP

## Slide 40: Server Hardware Requirements
Equip server with fastest CPU, as much RAM as possible, as much disk space as it will hold, and fastest NIC available
  Windows 2000 Server and Windows Server 2003 handle up to 32 CPUs in single system
  Specialized versions handle 64 or more processors

## Slide 41: Application Servers
Supply server side of client/server applications
Provide processing service and handle requests for file or print services
  Example: database server supplies query-processing and data-analysis facilities; repository for huge amounts of data within database

## Slide 42: Communication Servers
Allow users outside network to access network’s resources (inbound communications)
Sometimes permit users on network to access resources outside network (outbound communications)
Users may dial into network with modem
  Example: Windows 2000/2003 Server includes Remote Routing and Access Server (RRAS)

## Slide 43: Domain Controllers/ Directory Servers
Let users locate, store, and secure information about network and its resources
  Windows Servers combine computers, users, groups, and resources into logical domains

## Slide 44: Domain Controllers/ Directory Servers (continued)
Domain controller or directory server handles logon service
  By logging onto domain, user has access to all permitted resources and information
  Windows 2000/2003 Server and NetWare 4.x and newer versions include software to let server function as domain controller or directory server
  Linux directory service is called NIS

## Slide 45: Fax Servers
Manage fax traffic on network
Receive incoming faxes via telephone
Distribute faxes to recipients
Collect outgoing faxes to send via telephone
Must have at least one fax modem interface
Third-party vendors supply software to create Windows, NetWare, or Linux-based fax servers

## Slide 46: File and Print Servers
Provide basic network file storage and retrieval
Provide access to networked printers
Users run applications locally but keep data files on server and print hard-copies
Any Windows, NetWare, or Linux server can act as file and print server

## Slide 47: Mail Servers
Handle e-mail messages
Provide “store and forward” services
Hold incoming e-mail messages until users access them
Can hold outgoing e-mail messages until forwarded to their destinations
Microsoft Exchange Server runs on Windows 2000/2003; NetWare and Linux use other e-mail server programs

## Slide 48: Web Servers
Has gained popularity faster than any other single service
Many companies use WWW and TCP/IP protocol to distribute information via the Internet
May set up Web server to handle Internet traffic
  Windows .NET Server and Windows 2000 Server include Internet Information Server (IIS), a complete Web server
  NetWare versions 4.x and 5.x include Netscape Web server
  Apache Web server is available free for Linux

## Slide 49: Web-Based Networks
Internet and the WWW are becoming part of our everyday lives
Most computers are connected to Internet
Handheld devices such as cell phones and PDAs are connected through wireless communications
Cable modems and high-speed connections are common at work and home
New technologies such as Microsoft .NET will further integrate Web into our lives so that the Web is the network

## Slide 50: .NET Computing
Uses Web to deliver information and applications; allows devices to communicate and share data
Permits handheld computers to transfer information to and from network server using the Web
Allows transfer of information with unprecedented ease and convenience

## Slide 51: Web-Enabled Devices
WPANs include many Web-enabled devices that can transmit information via the Internet
Other devices are becoming Web-enabled such as automobiles with wireless navigation systems
Networking paradigm is shifting from clients and servers to Web-enabled or not Web-enabled
  Client will be any Web-enabled device that needs information
  Server will be any Web-enabled device that provides information

## Slide 52: Selecting the Right Type of Network
Choose peer-to-peer networking only if all these conditions are true:
  Network includes no more than 10 users
  All networked machines are close enough to form a single LAN
  Budget considerations are paramount
  No specialized servers are needed

## Slide 53: Selecting the Right Type of Network (continued)
Choose server-based network when one or more of the following conditions is true:
  More than 10 users share network access
  Centralized control, security, resource management, or backup is desirable
  Need specialized servers
  Heavy demands for network resources
  Use Internetwork or require WAN access
Consider future growth
  Even if peer-to-peer network serves current needs, may be best to implement server-based network

## Slide 54: ACTIVITY
Download and Install Packet Tracer: Link
https://www.netacad.com/resources/lab-downloads?courseLang=en-US
Set up a small physical network using basic networking equipment.
Use Packet Tracer to simulate different network topologies.

## Slide 55: End