## Slide 1: Transmission Media and Network Hardware/Software
Topic 2
Notes: NOTE:
To change the image on this slide, select the picture and delete it. Then click the Pictures icon in the placeholder to insert your own image.

## Slide 2: Transmission Media
Transmission media refers to the physical or wireless pathways used to transmit data from one device to another in a network.
It can be broadly categorized into guided (wired) and unguided (wireless) media.

## Slide 3: a). Guided Media (Wired)
Guided media involves physical cables that guide data signals along a predefined path. Examples
Twisted Pair Cables
Coaxial Cable
Fiber Optic Cable

## Slide 4: 1. Twisted Pair Cables
Description: Consists of pairs of insulated copper wires twisted together to reduce electromagnetic interference.
Types:
  Unshielded Twisted Pair (UTP): Commonly used in Ethernet networks.
  Shielded Twisted Pair (STP): Provides better shielding, used in industrial environments.

## Slide 6: Twisted Pair Cables
Applications: Telephone lines, LANs.
Advantages: Cost-effective, easy to install.
Disadvantages: Limited bandwidth, susceptible to interference.

## Slide 7: 2. Coaxial Cable
Description: A single copper conductor surrounded by insulation, shielding, and an outer jacket.
Applications: Cable TV, broadband internet.
Advantages: High resistance to interference, good bandwidth.
Disadvantages: Bulkier, more expensive than twisted pair.

## Slide 9: 3. Fiber Optic Cable
Description: Uses glass or plastic fibers to transmit data as light signals.
Applications: High-speed internet, long-distance communications.
Advantages: Immune to electromagnetic interference, very high bandwidth.
Disadvantages: Expensive, delicate, and requires specialized installation.

## Slide 11: b). Unguided Media (Wireless)
Unguided media involves data transmission through the air or vacuum without physical cables.
Terrestrial Microwave
Satellite Microwave
Radio Waves
Infrared (IR)

## Slide 12: 1. Terrestrial Microwave
Description: Uses high-frequency radio waves for line-of-sight communication.
Applications: Long-distance telephone and TV relay.
Advantages: High bandwidth, relatively inexpensive.
Disadvantages: Requires line of sight, affected by weather conditions.

## Slide 14: 2. Satellite Microwave
Description: Communication via satellites in geostationary orbit.
Applications: Global television broadcasts, GPS, internet.
Advantages: Wide coverage area, supports multiple users.
Disadvantages: High latency, expensive.

## Slide 16: 3. Radio Waves
Description: Low-frequency waves used for wireless communication.
Applications: AM/FM radio, mobile phones, Wi-Fi.
Advantages: Wide area coverage, no need for line of sight.
Disadvantages: Susceptible to interference.

## Slide 18: 4. Infrared (IR)
Description: Uses infrared light for short-range communication.
Applications: Remote controls, short-range networking.
Advantages: Simple and inexpensive.
Disadvantages: Limited range, requires line of sight.