## Slide 1: Network Protocols/standards and Services
Topic 4 and 5
Notes: NOTE:
To change the image on this slide, select the picture and delete it. Then click the Pictures icon in the placeholder to insert your own image.

## Slide 2: Network standards
Network standards are a set of rules, protocols, and guidelines that define how devices communicate and interact within a network.
These standards ensure interoperability, compatibility, and reliability of network components, regardless of the manufacturer.
OSI MODEL and DOD(TCP/IP) Model

## Slide 3: Importance of Network Standards
Interoperability – Allows devices from different manufacturers to communicate seamlessly.
Reliability – Ensures stable and predictable network performance.
Scalability – Facilitates network expansion without compatibility issues.
Security – Establishes protocols for secure data transmission.
Efficiency – Optimizes data transmission and resource usage.

## Slide 4: The OSI Model
The Open Systems Interconnection (OSI) Model is a conceptual framework used to understand and implement standard protocols in network communications.
It was developed by the International Organization for Standardization (ISO) in 1984 to facilitate interoperability between different network devices and technologies.
Has 7 layers and Each layer has a specific role and communicates with the layers above and below it.

## Slide 5: The Seven Layers of the OSI Model

## Slide 6
All People Seem To Need Data Processing

## Slide 9: 1. Physical Layer (Layer 1)
Function: Deals with the physical connection between devices and the transmission of raw bit streams over a physical medium.
Responsibilities
  Transmits bits (0s and 1s) over cables, radio waves, or fiber optics.
  Defines physical characteristics like cables, connectors, and signal types.
  Handles voltage levels, data rates, and physical topology (e.g., bus, star, ring).
Examples: Ethernet cables, fiber optics, hubs, repeaters.

## Slide 10: 2. Data Link Layer (Layer 2)
Function: Ensures reliable data transfer across the physical link and handles error detection and correction.
Responsibilities:
  Packages data into frames for transmission.
  Provides MAC (Media Access Control) addressing for device identification.
  Implements error detection using techniques like CRC (Cyclic Redundancy Check).
  Manages flow control to prevent overwhelming the receiver.

## Slide 11
Sub-layers:
  MAC Layer: Controls how devices access the medium.
  LLC (Logical Link Control) Layer: Manages error checking and frame synchronization.
Examples: Switches, bridges, Ethernet protocols.

## Slide 12: 3. Network Layer (Layer 3)
Function: Manages device addressing, routing, and packet forwarding between different networks.
Responsibilities:
  Assigns logical addresses (e.g., IP addresses) to devices.
  Determines the best path for data delivery using routing protocols.
  Fragments and reassembles packets for transmission.
Examples: Routers, IP (Internet Protocol), ICMP (Internet Control Message Protocol).

## Slide 13: 4. Transport Layer (Layer 4)
Function: Ensures reliable, end-to-end communication and data integrity.
Responsibilities:
  Segments data into smaller units called segments (TCP) or datagrams (UDP).
  Provides error recovery, flow control, and retransmission of lost packets.
  Establishes, maintains, and terminates connections (e.g., TCP three-way handshake).

## Slide 14
Protocols:
  TCP (Transmission Control Protocol): Reliable, connection-oriented.
  UDP (User Datagram Protocol): Unreliable, connectionless.
Examples: TCP, UDP, SCTP (Stream Control Transmission Protocol).

## Slide 15: 5. Session Layer (Layer 5)
Function: Manages sessions (connections) between applications.
Responsibilities:
  Establishes, maintains, and terminates communication sessions.
  Synchronizes data exchange and manages dialog control (e.g., half-duplex, full-duplex).
  Handles session recovery in case of interruptions.
Examples: NetBIOS, RPC (Remote Procedure Call), PPTP (Point-to-Point Tunneling Protocol).

## Slide 16: 6. Presentation Layer (Layer 6)
Function: Translates data into a format the application layer can understand.
Responsibilities:
  Handles data encryption, decryption, and compression.
  Translates between different data formats (e.g., ASCII to Unicode).
  Ensures data is presented correctly to the application layer.
Examples: SSL/TLS (encryption), JPEG, MPEG, GIF (data formatting).

## Slide 17: 7. Application Layer (Layer 7)
Function: Provides network services directly to end-user applications.
Responsibilities:
  Enables communication between software applications and the network.
  Provides protocols for specific services like email, file transfer, and web browsing.
Examples: HTTP/HTTPS (web browsing), FTP (file transfer), SMTP (email), DNS (domain name resolution).

## Slide 18: How Data Flows Through the OSI Model

## Slide 22: 1. Encapsulation
Data moves down the OSI layers from the Application Layer to the Physical Layer.
Each layer adds its own header (and sometimes trailer) to the data, creating a Protocol Data Unit (PDU).
  Application Layer: Data
  Transport Layer: Segment (TCP) or Datagram (UDP)
  Network Layer: Packet
  Data Link Layer: Frame
  Physical Layer: Bits

## Slide 23: 2. Decapsulation
At the receiving end, data moves up the OSI layers from the Physical Layer to the Application Layer.
Each layer removes its header and processes the data before passing it to the next layer.

## Slide 24: Advantages of the OSI Model
Standardization: Provides a universal framework for network communication.
Interoperability: Ensures devices from different vendors can work together.
Modularity: Each layer operates independently, simplifying troubleshooting and development.
Scalability: Allows networks to grow and adapt to new technologies.

## Slide 25: Real-World Applications of the OSI Model
Troubleshooting: Helps identify and isolate network issues by examining each layer.
Network Design: Guides the development of protocols and devices.
Education: Serves as a foundational concept for understanding networking.

## Slide 26
Layer | Function | Protocols/Devices
Application | Provides network services to applications | HTTP, FTP, SMTP, DNS
Presentation | Translates, encrypts, and compresses data | SSL/TLS, JPEG, MPEG
Session | Manages communication sessions | NetBIOS, RPC, PPTP
Transport | Ensures reliable data delivery | TCP, UDP
Network | Handles addressing and routing | IP, ICMP, Routers
Data Link | Manages frame transmission and error detection | Ethernet, Switches, MAC Addresses
Physical | Transmits raw bit streams | Cables, Hubs, Repeaters
Summary of OSI Layers

## Slide 27: D.O.D. Model (TCP/IP Model)

## Slide 28: D.O.D. Model (TCP/IP Model)
The Department of Defense (D.O.D.) Model, also known as the TCP/IP Model, is a simplified and practical framework for network communication.
The U.S. Department of Defense developed it in the 1970s to ensure reliable communication over diverse, interconnected networks.
This model is the foundation of the modern internet and consists of four layers, each with specific functions.

## Slide 31: 1. Network Access Layer (Layer 1)
Function: Combines the Physical and Data Link layers of the OSI Model. It handles the physical transmission of data and ensures reliable communication over the physical medium.
Responsibilities:
  Transmits raw bits over the network medium (e.g., cables, radio waves).
  Defines hardware addressing (e.g., MAC addresses).
  Manages access to the physical medium (e.g., Ethernet, Wi-Fi).
Examples: Ethernet, Wi-Fi, PPP (Point-to-Point Protocol), MAC addresses.

## Slide 32: 2. Internet Layer (Layer 2)
Function: Corresponds to the Network Layer of the OSI Model. It handles logical addressing, routing, and packet forwarding between devices across different networks.
Responsibilities:
  Assigns logical addresses (e.g., IP addresses) to devices.
  Routes packets between source and destination using routing protocols.
  Fragments and reassembles packets if necessary.

## Slide 33
Protocols:
  IP (Internet Protocol): Provides logical addressing and routing.
  ICMP (Internet Control Message Protocol): Handles error reporting and diagnostics (e.g., ping).
  ARP (Address Resolution Protocol): Maps IP addresses to MAC addresses.
Examples: IPv4, IPv6, Routers.

## Slide 34: 3. Transport Layer (Layer 3)
Function: Similar to the Transport Layer of the OSI Model. It ensures reliable, end-to-end communication and data integrity.
Responsibilities:
  Segments data into smaller units for transmission.
  Provides error detection, correction, and flow control.
  Establishes, maintains, and terminates connections.

## Slide 35
Protocols:
  TCP (Transmission Control Protocol): Reliable, connection-oriented communication with error recovery.
  UDP (User Datagram Protocol): Unreliable, connectionless communication for faster transmission.
Examples: TCP, UDP, SCTP (Stream Control Transmission Protocol).

## Slide 36: 4. Application Layer (Layer 4)
Function: Combines the Session, Presentation, and Application layers of the OSI Model. It provides high-level protocols for applications to communicate over the network.
Responsibilities:
  Enables communication between software applications and the network.
  Provides protocols for specific services like web browsing, email, and file transfer.

## Slide 37
Protocols:
  HTTP/HTTPS: Web browsing.
  FTP: File transfer.
  SMTP: Email transmission.
  DNS: Domain name resolution.
Examples: Web browsers, email clients, DNS servers.

## Slide 38: How Data Flows Through the D.O.D. Model
Encapsulation
  Data moves down the layers from the Application Layer to the Network Access Layer.
  Each layer adds its own header (and sometimes trailer) to the data, creating a Protocol Data Unit (PDU).
    Application Layer: Data
    Transport Layer: Segment (TCP) or Datagram (UDP)
    Internet Layer: Packet
    Network Access Layer: Frame

## Slide 39
2. Decapsulation:
At the receiving end, data moves up the layers from the Network Access Layer to the Application Layer.
Each layer removes its header and processes the data before passing it to the next layer.

## Slide 40
Layer | Protocols
Application Layer | HTTP, HTTPS, FTP, SMTP, DNS, Telnet, SSH, SNMP
Transport Layer | TCP, UDP
Internet Layer | IP, ICMP, ARP, IGMP
Network Access Layer | Ethernet, Wi-Fi, PPP, MAC Addresses
Key Protocols in the D.O.D. Model

## Slide 41: Advantages of the D.O.D. Model
Simplicity: Fewer layers make it easier to implement and understand.
Practicality: Designed for real-world use, especially in the context of the internet.
Flexibility: Supports a wide range of protocols and technologies.
Scalability: Adapts well to the growth of the internet and emerging technologies.

## Slide 42: Real-World Applications of the D.O.D. Model
Internet Communication: The D.O.D. Model is the foundation of the internet, enabling global connectivity.
Network Design: Guides the development of protocols and devices.
Troubleshooting: Helps identify and resolve network issues by examining each layer.

## Slide 43
Layer | Function | Protocols/Devices
Application | Provides high-level protocols for applications | HTTP, FTP, SMTP, DNS
Transport | Ensures reliable data delivery | TCP, UDP
Internet | Handles logical addressing and routing | IP, ICMP, Routers
Network Access | Manages physical transmission and hardware addressing | Ethernet, Wi-Fi, MAC Addresses
Summary of D.O.D. Layers

## Slide 44: Network Services

## Slide 45: Network Services
Network services are essential components of modern networking that enable communication, resource sharing, and management across devices.

## Slide 46: 1. NAT (Network Address Translation)
Definition: NAT is a technique used to map private IP addresses to a public IP address, allowing multiple devices on a local network to share a single public IP for internet access.
Purpose:
  Conserves IPv4 addresses by allowing multiple devices to use one public IP.
  Enhances security by hiding internal IP addresses from external networks.

## Slide 47
Types of NAT:
  Static NAT: Maps a private IP address to a specific public IP address (one-to-one).
  Dynamic NAT: Maps private IP addresses to a pool of public IP addresses (many-to-many).
  PAT (Port Address Translation): Maps multiple private IP addresses to a single public IP address using different ports (many-to-one).
Use Case: Home routers, corporate networks, and ISPs use NAT to manage IP address allocation and improve security.

## Slide 48: 2. DHCP (Dynamic Host Configuration Protocol)
Definition: DHCP is a network management protocol used to automatically assign IP addresses and other network configuration parameters (e.g., subnet mask, default gateway, DNS server) to devices on a network.
Purpose:
  Simplifies network administration by automating IP address allocation.
  Reduces manual configuration errors and IP conflicts.

## Slide 49: How It Works
  DHCP Discover: The client broadcasts a request for an IP address.
  DHCP Offer: The DHCP server responds with an available IP address.
  DHCP Request: The client requests the offered IP address.
  DHCP Acknowledgment: The server confirms the allocation and provides additional configuration details.

## Slide 50: Components
  DHCP Server: Manages IP address allocation.
  DHCP Client: Requests and uses the assigned IP address.
  IP Lease: The duration for which an IP address is assigned to a client.
Use Case: Used in home networks, offices, and large enterprises to manage IP addressing efficiently.

## Slide 51: 3. DNS (Domain Name System)
Definition: DNS is a system that translates human-readable domain names (e.g., www.example.com) into machine-readable IP addresses (e.g., 192.168.1.1).
Purpose:
  Simplifies access to websites and services by using memorable domain names instead of numeric IP addresses.
  Enables load balancing and fault tolerance by distributing requests across multiple servers.

## Slide 52
How It Works:
  The user enters a domain name in their browser.
  The DNS resolver queries the DNS server to find the corresponding IP address.
  The DNS server responds with the IP address, allowing the browser to connect to the website.

## Slide 53
Components:
  DNS Server: Stores domain name and IP address mappings.
  DNS Resolver: Queries the DNS server on behalf of the client.
  Root Servers: The top-level DNS servers that direct queries to the appropriate authoritative servers.
Use Case: Essential for internet browsing, email delivery, and accessing online services.

## Slide 54: 4. Web Server
Definition: A web server is a software or hardware system that hosts and delivers web pages and applications to clients over the internet or an intranet.
Purpose:
  Stores and serves website content (e.g., HTML, CSS, JavaScript, images).
  Processes client requests and sends responses using the HTTP/HTTPS protocol.

## Slide 55
Key Features:
  Supports static and dynamic content.
  Handles multiple client requests simultaneously.
  Provides security features like SSL/TLS encryption.
Examples:
  Software: Apache, Nginx, Microsoft IIS.
  Hardware: Dedicated servers or cloud-based hosting platforms.
Use Case: Hosting websites, web applications, and APIs.

## Slide 56: 5. Mail Server
Definition: A mail server is a system that handles the sending, receiving, and storage of emails.
Purpose:
  Manages email communication between users.
  Stores emails until they are retrieved by the recipient.
Key Protocols:
  SMTP (Simple Mail Transfer Protocol): Used for sending emails.
  POP3 (Post Office Protocol): Used for retrieving emails (deletes emails from the server after download).
  IMAP (Internet Message Access Protocol): Used for retrieving emails (keeps emails on the server).

## Slide 57
Components:
  Mail Transfer Agent (MTA): Handles email routing and delivery.
  Mail Delivery Agent (MDA): Delivers emails to the recipient's mailbox.
  Mail User Agent (MUA): The email client used by the user (e.g., Outlook, Gmail).
Examples: Microsoft Exchange, Postfix, Sendmail.
Use Case: Email communication in organizations and personal use.

## Slide 58: 6. File and Print Server
Definition: A file server stores and manages files, while a print server manages printers and print jobs in a network.
Purpose:
  Centralizes file storage and printer management for multiple users.
  Enables resource sharing and collaboration.
Key Features:
  File Server:
    Provides shared access to files and folders.
    Manages user permissions and access control.
  Print Server:
    Manages print queues and job scheduling.
    Allows multiple users to share a single printer.

## Slide 59
Examples:
  File Server: Windows File Server, Samba (Linux).
  Print Server: CUPS (Common Unix Printing System), Windows Print Server.
Use Case: Used in offices, schools, and organizations to share resources efficiently.

## Slide 60: Other Examples of Network Services
FTP (File Transfer Protocol) – Enables file sharing and transfer.
VoIP (Voice over IP) – Supports voice calls over the internet.
VPN (Virtual Private Network) – Ensures secure remote access.
Cloud Services – Provides online storage, computing, and application hosting.

## Slide 61
Service | Purpose | Key Protocols/Components
NAT | Maps private IPs to a public IP for internet access | Static NAT, Dynamic NAT, PAT
DHCP | Automates IP address allocation | DHCP Server, IP Lease
DNS | Translates domain names to IP addresses | DNS Server, DNS Resolver
Web Server | Hosts and delivers web content | HTTP/HTTPS, Apache, Nginx
Mail Server | Manages email communication | SMTP, POP3, IMAP
File and Print Server | Centralizes file storage and printer management | Samba, CUPS, Windows File Server
Summary of Network Services

## Slide 62: Importance of Network Services
Communication: Enables data exchange between devices.
Efficiency: Automates tasks like IP address allocation and domain name resolution.
Resource Sharing: Enables shared access to files, printers, and applications.
Scalability: Supports the growth of networks and user demands.
Security: Provides authentication, encryption, and access control.
Remote Access: Supports remote connections for users and applications.

## Slide 63: Activity/Assignment
Map different networking protocols to corresponding OSI model layers.
Analyze and compare OSI and TCP/IP models.

## Slide 64: THANK you