## Slide 1: Addressing in Networks
Notes: NOTE:
To change the image on this slide, select the picture and delete it. Then click the Pictures icon in the placeholder to insert your own image.

## Slide 2
Network Addressing refers to the method of assigning unique identifiers to devices in a network to enable communication between them.
It is a fundamental concept in networking that ensures data is sent to the correct destination.

## Slide 3: 1. MAC Address
A Media Access Control (MAC) address is a unique identifier assigned to a network interface card (NIC) of a device.
It is used for communication within a network segment/ local network (LAN).
The MAC address operates at the Data Link Layer (Layer 2) of the OSI model.

## Slide 4: Structure of a MAC Address
Format: 48-bit address, Typically represented as six groups of two hexadecimal digits, separated by colons or hyphens (e.g., 00:1A:2B:3C:4D:5E or 00-1A-2B-3C-4D-5E)
Composition:
The first 24 bits (first 3 octets) represent the Organizationally Unique Identifier (OUI) assigned by IEEE to a manufacturer.
The last 24 bits (last 3 octets) are uniquely assigned by are assigned by the manufacturer and represent the device identifier.

## Slide 5: Functions of MAC Address
Device Identification: Ensures every networked device has a unique address.
Local Communication: Used for communication within the same LAN segment.
Security: Can be used in MAC filtering to control network access.

## Slide 6: Characteristics
Uniqueness: Each MAC address is globally unique, assigned by the manufacturer.
Hardware-Based: Tied to the physical hardware of the device.
Non-Routable: MAC addresses are only used within a local network and cannot be routed across different networks.

## Slide 7: MAC Address Types
Unicast MAC Address: Address assigned to a specific NIC.
Multicast MAC Address: Used for sending data to multiple devices.
Broadcast MAC Address: FF:FF:FF:FF:FF:FF, used to send data to all devices in a network.

## Slide 8: 2. IP Addressing, Classes, and Subnetting
IP Address (Internet Protocol Address)
Definition: An IP address (Internet Protocol address) is a unique numerical identifier assigned to each device connected to a computer network that uses the Internet Protocol for communication.
Purpose:
Identification of the host or network interface – It uniquely identifies a device on a network.
Location addressing – It provides the device’s location in the network, enabling data to be routed between devices.

## Slide 9: IP Address Assignment Methods
IP addresses can be assigned using different methods depending on the network type and management requirements.

## Slide 10: 1. Static IP Addressing:
Definition: Manually assigning a fixed IP address to a device.
Advantages:
  Provides a fixed, permanent IP address.
  Suitable for servers, printers, and network devices.
Disadvantages:
  Time-consuming to configure.
  Prone to human error/duplicates
  Inefficient for large networks.

## Slide 11: 2. Dynamic IP Addressing (DHCP)
Definition: Automatically assigning IP addresses to devices using a DHCP (Dynamic Host Configuration Protocol) server.
Advantages:
  Simplifies IP address management.
  Reduces configuration errors.
  Efficient for large networks.
Disadvantages:
  IP addresses may change over time.
  Requires a DHCP server.
  Devices might lose connectivity if no DHCP server is available

## Slide 12: DHCP (Dynamic Host Configuration Protocol):
Function: Automatically assigns IP addresses, subnet masks, default gateways, and other network parameters to devices.
Process:
  Discover: Client broadcasts a DHCP Discover message.
  Offer: DHCP server responds with a DHCP Offer message.
  Request: Client requests the offered IP address.
  Acknowledge: DHCP server confirms the assignment.
Lease Time: The duration for which an IP address is assigned to a device.

## Slide 13: 3. APIPA (Automatic Private IP Addressing)
Definition: A fallback mechanism used when a DHCP server is unavailable.
Range: 169.254.0.1 to 169.254.255.254.
Purpose: Allows devices to communicate within a local network without manual configuration.

## Slide 14: 4. Link-Local Addressing (IPv6)
Assigns an automatic, non-routable address (FE80::/10 range) for local communication.
Pros: Useful for device-to-device communication without a DHCP server.
Cons: Cannot be used for internet communication.

## Slide 15: IP Versions
IPv4:
32-bit address, represented as four decimal numbers separated by dots (e.g., 192.168.1.1).
Supports approximately 4.3 billion unique addresses.
IPv6:
128-bit address, represented as eight groups of four hexadecimal digits (e.g., 2001:0db8:85a3:0000:0000:8a2e:0370:7334).
Provides a vastly larger address space.

## Slide 16: IP Address Classes (IPv4)
IPv4 addresses are divided into five classes (A, B, C, D, E) based on the value of the first octet:

## Slide 18
Class | First Octet Range | Default Subnet Mask | Number of Hosts
A | 1 - 126 | 255.0.0.0 | ~16 million
B | 128 - 191 | 255.255.0.0 | ~65,000
C | 192 - 223 | 255.255.255.0 | 254
D | 224 - 239 | N/A (Multicast) | N/A
E | 240 - 255 | N/A (Reserved) | N/A

## Slide 20: Reserved IP Addresses:
Private IP Addresses:
Used within private networks (e.g., 10.0.0.0/8, 172.16.0.0/12, 192.168.0.0/16).
Loopback Address:
127.0.0.1- 127.255.255.255, used for testing network software and cannot be used for regular networking.
Public IP Addresses:
Globally unique and assigned by ISPs (Internet Service Providers).

## Slide 24: Subnet Mask
A subnet mask is a number used in networking to separate an IP address into two parts:
    the network portion (identifies the network)
    the host portion (identifies a specific device on that network)
A subnet mask works together with an IP address to determine:
    Which network the device belongs to
    Which devices are in the same network
Uses 1s (255) to represent the network part and It uses 0s to represent the host part
Example
  IP Address: 192.168.1.10 ->>>>Subnet Mask: 255.255.255.0
      Network part: 192.168.1-->>>>>>Host part: 10

## Slide 25: Default Subnet Mask
A default subnet mask is the standard subnet mask assigned to an IP address based on its class (Class A, B, or C) in classful networking.
It is used to separate the network portion from the host portion of an IP address.

## Slide 27: Task: Identify the class of IP addresses and the IP address belonging to the same network
A----10.1.0.1
B----10.25.10.5
C----10.100.50.20
D----10.200.1.10
D----172.16.1.1
E----172.20.10.15
F----172.16.100.5
G----172.30.50.25
H----192.168.1.1
I----192.168.10.20
J----192.168.10.5
K----192.168.100.25

## Slide 28
Number of Networks and Hosts
Class A IP addresses can support up to 16 million hosts on 127 networks.
The number of hosts is calculated as (2^{24} - 2 = 16,777,214), and
The number of networks is calculated as (2^7 - 2 = 126) (excluding the addresses 0.0.0.0 and 127.0.0.0, which are reserved).

## Slide 29: Subnetting
Definition: The process of dividing a larger network into smaller, more manageable subnetworks (subnets).
Purpose:
  Improves network performance and reduces congestion.
  Enhances security by isolating network segments.
  Efficiently utilizes IP addresses.

## Slide 30: CIDR Notation
CIDR (Classless Inter-Domain Routing):-Total Number of Network Bits
Default CIDR Value: Class A=/8, Class B=/16, Class C=/24
represents subnet masks in a concise format/short form
192.168.1.0/24 → Subnet mask 255.255.255.0
172.0.0.0/16 → Subnet mask 255.255.0.0

## Slide 31: Steps to Subnet
Determine the Subnet Mask
Calculate the Number of Networks.
Identify the IP Address for each network(Block Size).
Identify the Number of Hosts in each Network.
Locate the Network ID and Broadcast ID
Assign IP addresses to subnets and hosts.

## Slide 32: Subnet Calculation Example
If given 192.168.1.0/26:
Subnet Mask: 255.255.255.192
Total Subnets: 4 (192.168.1.0, 192.168.1.64, 192.168.1.128, 192.168.1.192)
Hosts per Subnet: 62 (each subnet has 2^6 - 2 usable hosts).

## Slide 33
Default Subnet Mask 255 |  |  |  |  |  |  |  | 255 |  |  |  |  |  |  |  | 255 |  |  |  |  |  |  |  | 0 |  |  |  |  |  |  | 
27 | 26 | 25 | 24 | 23 | 22 | 21 | 20 | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20 | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20 | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0
192.168.1.0/26
1. Subnet Mask: 255.255.255.192

## Slide 34: 2. How to find the number of networks
= 2^n [ Where n is the total Number of HOST bits borrowed or subnet bits borrowed]
=2^2= 4 Networks (You can create 4 Networks)

## Slide 35: 3. How to find the number of IP Addresses on each network
= 2^h [ Where h is the total Number of remaining HOST bits]
=2^6=64( On each Network you will have 64 IP Addresses)
Block Size=2^6=64

## Slide 36: 4. HOW TO FIND THE NUMBER OF HOSTS IN EACH NETWORK
= 2h-2 [ Where h is the Number of remaining HOST bits]
=2^6-2 =62 ( You will have 62 Host IP Addresses on Each Network)
The total number of IP Address you can assign to devices/host on a Network
Less by 2-Because
First IP- Reserved for the Network ID,
Last IP– Reserved for the Broadcast ID

## Slide 37
Network ID | Usable Host IDs | Broadcast ID
1. 192.168.1.0 | 192.168.1.1 - 192.168.1.62 | 192.168.1.63
2. 192.168.1.64 | 192.168.1.65 - 192.168.1.126 | 192.168.1.127
3. 192.168.1.128 | 192.168.1.129 - 192.168.1.190 | 192.168.1.191
4. 192.168.1.192 | 192.168.1.193- 192.168.1.254 | 192.168.1.255

## Slide 38: Subnetting Class-B
172.16.64.0/18
Find Subnet Mask?
Find the number of Networks.
Find the Number of IP Addresses on each Network
Find the Block Size.
Find the Number of Usable Hosts in each Network
Network ID and
Broadcast ID?

## Slide 39
Default Subnet Mask 255 |  |  |  |  |  |  |  | 255 |  |  |  |  |  |  |  | 0 |  |  |  |  |  |  |  | 0 |  |  |  |  |  |  | 
27 | 26 | 25 | 24 | 23 | 22 | 21 | 20 | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20 | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20 | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
172.16.64.0/18
Subnet Mask: 255.255.192.0
No. of Networks: 4
No. of IP on each Network=2^h=2^14=16,384
Block Size: =(256-192)=64 OR the Value of Last borrowed subnet bit(2^6)
No. of Hosts: (2^h -2) =(2^14)-2 =16,382

## Slide 40
Network ID | Usable Host IDs | Broadcast ID
1. 172.16.0.0 | 172.16.0.1 - 172.16.63.254 | 172.16.63.255
2. 172.16.64.0 | 172.16.64.1 - 172.16.127.254 | 172.16.127.255
3. 172.16.128.0 | 172.16.128.1 - 172.16.191.254 | 172.16.191.255
4. 172.16.192.0 | 172.16.192.1 - 172.16.255.254 | 172.16.255.255
N/B: Block Size is added to the octet with the last subnet bit

## Slide 41: Class B Subnetting -Activity
172.168.10.0/28
Find Subnet Mask?
Find the number of Networks.
Find the Number of IP Addresses on each Network
Find the Block Size.
Find the 1st , 2nd , 3rd ,4th and Last Network ID, Broadcast ID and Usable Hosts IP Address range in each Network.

## Slide 42: Subnetting Class-A
10.0.0.0/10
Find Subnet Mask?
Find the number of Networks.
Find the Number of IP Addresses on each Network
Find the Block Size.
Find the Number of Usable Hosts in each Network
Network ID and
Broadcast ID?

## Slide 43
Default Subnet Mask 255 |  |  |  |  |  |  |  | 0 |  |  |  |  |  |  |  | 0 |  |  |  |  |  |  |  | 0 |  |  |  |  |  |  | 
27 | 26 | 25 | 24 | 23 | 22 | 21 | 20 | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20 | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20 | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
10.0.0.0/10
Subnet Mask: 255.192.0.0
No. of Networks: 2^n =(2^2)=4
No. of IP on each Network=2^h=4,194,304
Block Size: =(256-192)=64 OR the Value of Last borrowed subnet bit(2^6)
No. of Hosts: (2^h -2) =(2^22)-2 =4,194,302

## Slide 44
Network ID | Usable Host IDs | Broadcast ID
1. 10.0.0.0 | 10.0.0.1 - 10.63.255.254 | 10.63.255.255
2. 10.64.0.0 | 10.64.0.1 - 10.127.255.254 | 10.127.255.255
3. 10.128.0.0 | 10.128.0.1 - 10.191.255.254 | 10.191.255.255
4. 10.192.0.0 | 10.192.0.1 - 10.255.255.254 | 10.255.255.255
N/B: Block Size is added to the octet with the last subnet bit

## Slide 45: Class A-Activity
a) 10.0.0.0/18
b) 10.0.0.0/30
Find Subnet Mask?
Find the number of Networks.
Find the Number of IP Addresses on each Network(Block Size).
Find the 1st , 2nd , 3rd ,4th and 10th Network ID, Broadcast ID and Usable Hosts IP Address range in each Network

## Slide 46: Variable Length Subnet Masking (VLSM)
Subnetting Continued
Notes: NOTE:
To change the image on this slide, select the picture and delete it. Then click the Pictures icon in the placeholder to insert your own image.

## Slide 47: Introduction to VLSM
Variable Length Subnet Masking (VLSM) is subnetting technique that allows different subnet masks to be used within the same network.
This optimizes IP address allocation by assigning subnet sizes based on the actual number of required hosts.

## Slide 48: Why Use VLSM?
Efficient IP address utilization
Flexibility in subnet design
Reduces IP address wastage
Allows hierarchical network structuring
Supports diverse network requirements

## Slide 49: How VLSM Works
VLSM allows a network to be divided into subnets of varying sizes by using different subnet masks.
Unlike traditional subnetting, which uses a fixed-size subnet mask, VLSM provides more control over IP allocation.

## Slide 50
Feature | Fixed Length Subnet Mask (FLSM) | Variable Length Subnet Mask (VLSM)
Subnet Size | All subnets are equal | Different subnets have different sizes
Address Wastage | High | Low
Flexibility | Low | High
IP Efficiency | Poor | Optimized
Key Differences Between FLSM and VLSM

## Slide 51: Benefits of VLSM
Optimizes IP address allocation
Supports efficient routing
Reduces unnecessary IP wastage
Helps in hierarchical subnetting
Enhances scalability

## Slide 52: Applications of VLSM
Enterprise networks with multiple departments.
Internet Service Providers (ISPs) allocating addresses to customers.
Data centers with varying server requirements.
WAN and LAN designs.

## Slide 53: VLSM Subnetting Process
Step 1: Identify Network Requirements
Determine the number of subnets and hosts required per subnet. Prioritize larger subnets first.
Step 2: Assign Subnet Masks
Use appropriate subnet masks for each subnet based on the required number of hosts.
Step 3: Allocate IP Ranges
Assign IP address ranges based on the subnet mask chosen for each segment.
Step 4: Validate Addressing Scheme
Ensure there are no overlaps and that the network can route traffic correctly.

## Slide 54: Example of VLSM Subnetting
A company has been assigned the network 192.168.1.0/24. It needs the following subnets:
Head Office: 50 hosts
Branch Office 1: 25 hosts
Branch Office 2: 10 hosts
Point-to-Point Link: 2 hosts

## Slide 55: Step 1: Start with the Largest Subnet
Head Office: Requires 50 hosts
  Use /26 subnet (supports 62 hosts)
  Subnet: 192.168.1.0/26 (Range: 192.168.1.1 - 192.168.1.62)

## Slide 56: Step 2: Assign the Next Largest Subnet
Branch Office 1: Requires 25 hosts
  Use /27 subnet (supports 30 hosts)
  Subnet: 192.168.1.64/27 (Range: 192.168.1.65 - 192.168.1.94)

## Slide 57: Step 3: Assign the Next Smallest Subnet
Branch Office 2: Requires 10 hosts
  Use /28 subnet (supports 14 hosts)
  Subnet: 192.168.1.96/28 (Range: 192.168.1.97 - 192.168.1.110)

## Slide 58: Step 4: Assign the Smallest Subnet
Point-to-Point Link: Requires 2 hosts
  Use /30 subnet (supports 2 hosts)
  Subnet: 192.168.1.112/30 (Range: 192.168.1.113 - 192.168.1.114)

## Slide 59: Step 5: Remaining IP Addresses
After allocation, we still have available IP addresses for future use.

## Slide 60: Practice Questions
Given 192.168.10.0/24, design subnets for 100, 50, 20, and 5 hosts using VLSM.
What is the next available subnet after 172.16.1.0/28?
Calculate the subnet mask for a subnet needing at least 200 hosts.
Calculate the subnet mask for a subnet requiring 120 hosts.
Notes: 1.
Subnet A (100 hosts):
Calculate CIDR: 2(32−CIDR)−2≥1002(32−CIDR)−2≥100 → /25 (128 hosts)
Subnet Mask: 255.255.255.128
Network Address: 192.168.10.0/25
Usable Range: 192.168.10.1 - 192.168.10.126
Broadcast Address: 192.168.10.127
Subnet B (50 hosts):
  Required hosts: 50
  Calculate CIDR: /26 (64 hosts)
  Subnet Mask: 255.255.255.192
  Network Address: 192.168.10.128/26
  Usable Range: 192.168.10.129 - 192.168.10.190
  Broadcast Address: 192.168.10.191
Subnet C (20 hosts):
  Required hosts: 20
  Calculate CIDR: /27 (32 hosts)
  Subnet Mask: 255.255.255.224
  Network Address: 192.168.10.192/27
  Usable Range: 192.168.10.193 - 192.168.10.222
  Broadcast Address: 192.168.10.223
Subnet D (5 hosts):
  Required hosts: 5
  Calculate CIDR: /29 (8 hosts)
  Subnet Mask: 255.255.255.248
  Network Address: 192.168.10.224/29
  Usable Range: 192.168.10.225 - 192.168.10.230
  Broadcast Address: 192.168.10.231
2. Next Subnet: 172.16.1.16/28
3Subnet Mask:
  CIDR: /24
  Subnet Mask: 255.255.255.0

## Slide 61: ACTIVITY 1
You have been employed as a network Administrator at a coffee Shop, and your Supervisor provided you with the Network ID 192.168.4.0/25 to create two (2) separate Networks one for the Office and one for the Storage Room. You are required to list each
Network IDs,
Subnet Mask,
Usable Host IDs and
Broadcast IDs

## Slide 62: ACTIVITY 2
Design and implement the above network using Cisco Packet Tracer.

## Slide 63: Subnetting Video Tutorial Link
1. https://youtu.be/q7wNcYliJ1Q
2. https://youtu.be/rJUt2K6K_tA?si=lidupXCjVi-wLSu3
3. https://youtu.be/wwouydtPfJI?si=zXno0AIzrlHvQPeQ

## Slide 64: THANK you