## Slide 1: Practical-Cable Termination
Topic 10
Notes: NOTE:
To change the image on this slide, select the picture and delete it. Then click the Pictures icon in the placeholder to insert your own image.

## Slide 2: Terminating Ethernet cables
A process of attaching connectors to cables for network connections.

## Slide 3: Tools and Materials
Bulk Ethernet Cable: Preferably CAT6 for higher performance, though CAT5e is also common. Ensure it is unshielded twisted pair (U/UTP) for standard applications.
RJ45 Connectors: Pass-through RJ45 connectors are recommended for ease of insertion.
Crimping Tool: A CAT6 crimping tool is essential, and some models include a built-in stripping tool, which can save time.
Cable Tester: Useful for verifying the cable’s functionality after termination, ensuring no connectivity issues.

## Slide 4: Tools and Materials-cont’d
Wire Cutters or Scissors: For trimming wires to length, a flush cutter is ideal for clean, angled cuts.
Wire Stripper: If the crimping tool doesn’t have this feature, a separate professional stripping tool is necessary.
Strain Relief Boots: Optional but recommended for protecting the connection and adding durability.

## Slide 6: Wiring Standards: T568A vs. T568B
Dictates the order of the eight wires inside the RJ45 connector. The main difference lies in the arrangement of the orange and green wire pairs:
T568A: Green pair in positions 1 and 2, Orange pair in positions 3 and 6. Preferred for backward compatibility with older phone systems and required for US federal contracts.
T568B: Orange pair in positions 1 and 2, Green pair in positions 3 and 6. More commonly used in modern networks due to its prevalence and compatibility with AT&T 258A color codes.
T568B: Recommended for new installations due to its widespread adoption.

## Slide 8: Common Mistakes and Best Practices
Excessive Untwisting: Untwisting the pairs too much can lead to crosstalk and signal degradation. Keep untwisting minimal, only enough to fit into the connector.
Nicked Conductors: Damaging wires during stripping can cause intermittent connectivity. Use sharp, precise tools and check for nicks/scratches.
Inconsistent Standards: Mixing T568A and T568B at cable ends can result in a non-functional connection. Always use the same standard throughout.
Poor Crimping: Ensure the crimping tool is fully engaged to secure all pins. A loose crimp can lead to connection failures.

## Slide 10: Steps Overview
Measure and cut the cable to the desired length, adding extra for the ends.
Strip the outer jacket to expose the wires, being careful not to damage them.
Arrange the wires in either T568A or T568B order, with T568B preferred for modern networks.
Insert the wires into an RJ45 connector, ensuring they are fully seated.
Use the crimping tool to secure the connector to the cable.
Repeat for the other end, ensuring consistency in wiring standard.
Test the cable with a tester to ensure it works.

## Slide 11: ACTIVITY
Create a cable for connecting two laptops
Create a cable for connecting a Computer and a Switch

## Slide 12: THANK you